## Slide 1
Building Natural Frequencies
By Tom Irvine
Vibrationdata

## Slide 2
Vibrationdata
Basic Definitions
The natural frequency is the frequency at which the system will vibrate if it is given an initial displacement and then allowed to undergo free vibration
It is also the frequency at which an exchange occurs between potential and kinetic energy
The natural frequency is the inverse of the period
The angular natural frequency is
Resonance occurs if a building’s natural frequency is excited by an earthquake, wind or some other source
Notes: 2

## Slide 3
3
Vibrationdata
Transamerica Pyramid Building
Direction | Loma Prieta Earthquake |  | Ambient Vibration | 
 | fn (Hz) | Damping | fn (Hz) | Damping
North-South | 0.28 | 4.9% | 0.34 | 0.8%
East-West | 0.28 | 2.2% | 0.32 | 1.4%
The Transamerica Pyramid is built from a steel frame, with a truss system at the base
The height is 850 ft (260 m)
Amplitude-dependent stiffness degradation and increased damping due to joint friction, connection slip, and soil–structure interaction
Çelebi, M., “Dynamic Characteristics of the Transamerica Pyramid Building” Earthquake Spectra, Vol. 7, No. 4, 1991
Notes: 3

## Slide 4
4
Vibrationdata
Pacific Park Plaza, Emeryville, CA
The Pacific Park Plaza height is 308 ft (94 meters)
It has a reinforced concrete moment-frame/shear-wall structure
Direction | Loma Prieta Earthquake |  | Ambient Vibration | 
 | fn (Hz) | Damping | fn (Hz) | Damping
North-South | 0.38 | 11.6% | 0.48 | 0.6%
East-West | 0.38 | 15.5% | 0.48 | 3.4%
Notes: 4

## Slide 5
Vibrationdata
Washington Monument
According to analyses cited by the United States Geological Survey (USGS), the fundamental resonant frequency of the 169 m (555 ft) tall obelisk is about 0.3 Hz
This is its lowest natural mode, corresponding to a very slow sway motion of the whole structure
In addition, smaller parts of the structure (notably the pyramidion at the top) have higher local resonant frequencies in the range of roughly 2.5 Hz to 5 Hz
Washington Monument Crack, Earthquake 2011
Notes: 5

## Slide 6
Vibrationdata
Eiffel Tower
First lateral bending mode: about 0.32 Hz (period ~3.1 s)
Second lateral bending mode: about 1.0 Hz.
Torsional mode: around 1.2 Hz (twisting motion)
Notes: 6

## Slide 7
Burj Khalifa

## Slide 8
Vibrationdata
Building Period Calculation Methods
Method | Basic Idea | Required Data | Pros | Cons | IASCE 7-22
ASCE Approximate Period | Empirical height-based formula | Total building height | Very simple | Ignores mass & stiffness | YES (§12.8.2.1)
 |  | Structural system type (for ) | No modeling required | Not building-specific | 
 |  |  | Always code-compliant for ELF | Often conservative | 
Rayleigh – Stiffness Form | Energy method using assumed mode shape and story stiffness | Story masses | Good first-mode estimate | Depends on assumed mode shape | YES (Permitted to compute T, subject to upper bound limits)
 |  | Story stiffnesses | Physically based | Approximate | 
 |  | Assumed mode shape | Moderate effort |  | 
Rayleigh – Force–Displacement Form | Use lateral force pattern and resulting story displacements: | Story masses | No stiffness matrix needed | Still approximate | YES (Commonly used to compute period from analysis results)
 |  | Lateral forces (e.g., ELF pattern) | Very practical for hand checks | Depends on displacement accuracy | 
 |  | Resulting story displacements | Works well with ELF output |  | 
Eigenvalue (Modal) Analysis | Solve generalized eigenvalue problem | Mass matrix | Exact solution for linear system | Requires full model | YES (Required for Modal Response Spectrum Analysis, §12.9)
Shear Building Eigenvalue Analysis |  | Stiffness matrix | No assumed mode shape | More computational effort | 
 |  |  | Provides all modes |  | 
Method | Basic Idea | Required Data | Pros | Cons | IASCE 7-22
 | Empirical height-based formula | Total building height | Very simple | Ignores mass & stiffness | YES (§12.8.2.1)
 |  |  | No modeling required | Not building-specific | 
 |  |  | Always code-compliant for ELF | Often conservative | 
Rayleigh – Stiffness Form | Energy method using assumed mode shape and story stiffness | Story masses | Good first-mode estimate | Depends on assumed mode shape | YES (Permitted to compute T, subject to upper bound limits)
 |  | Story stiffnesses | Physically based | Approximate | 
 |  | Assumed mode shape | Moderate effort |  | 
Rayleigh – Force–Displacement Form | Use lateral force pattern and resulting story displacements: | Story masses | No stiffness matrix needed | Still approximate | YES (Commonly used to compute period from analysis results)
 |  | Lateral forces (e.g., ELF pattern) | Very practical for hand checks | Depends on displacement accuracy | 
 |  | Resulting story displacements | Works well with ELF output |  | 
Eigenvalue (Modal) Analysis | Solve generalized eigenvalue problem | Mass matrix | Exact solution for linear system | Requires full model | YES (Required for Modal Response Spectrum Analysis, §12.9)
Shear Building Eigenvalue Analysis |  | Stiffness matrix | No assumed mode shape | More computational effort | 
 |  |  | Provides all modes |  | 

## Slide 9
Vibrationdata
Typical Natural Frequencies
System | 3–5 Story | 10–20 Story | 40+ Story
Steel Moment Frame | 1–2 Hz | 0.4–0.8 Hz | 0.1–0.3 Hz
RC Moment Frame | 1.2–2.5 Hz | 0.5–1.0 Hz | 0.15–0.4 Hz
RC Shear Wall | 2–4 Hz | 0.8–1.5 Hz | 0.2–0.5 Hz
Steel Braced Frame | 2–5 Hz | 1–2 Hz | 0.3–0.7 Hz
https://theconstructor.org/structural-engg/shear-wall-types-efficiency/6820/

## Slide 10
Vibrationdata
Natural Frequency Non-linearity
Building natural frequencies tend to decrease during an earthquake due to
  Microcracking (concrete)
  Connection microslip (steel)
  Nonstructural element participation
  Soil–structure interaction
  The natural frequencies often recover or partially recover post-event

## Slide 11
Vibrationdata
Typical Building Damping, Elastic Range
System | Ambient | Strong Motion
Steel Moment Frame | 0.5–2% | 2–5%
RC Moment Frame | 1–3% | 5–15%
Shear Wall | 1–2% | 4–10%
Damping increases with amplitude due to friction, cracking, structure-soil interaction (SSI)

## Slide 12
Vibrationdata
Building Period T
Short-period (acceleration-controlled)
Long-period (velocity-controlled)
Influences:
  Base shear magnitude
  Drift demand
  Distribution of lateral forces
Longer T → typically lower design base shear
Shorter T → higher base shear
Rule-of-Thumb Estimate (Quick Screening)
For moment frame buildings:
T ≈ 0.1 × ( number of stories )
Building Type | Height | Typical T (sec)
1–2 Story Wood Frame | 20–30 ft | 0.1 – 0.3
Low-Rise Masonry (2–3 story) | 25–40 ft | 0.2 – 0.5
3–5 Story Steel Moment Frame | 40–70 ft | 0.4 – 0.9
5–10 Story RC Moment Frame | 60–120 ft | 0.6 – 1.5
10–20 Story Steel Moment Frame | 120–250 ft | 1.2 – 3.0
20–40 Story RC Shear Wall Building | 250–500 ft | 2.5 – 5.5
Tall Flexible Steel Frame (40+ stories) | 500–800 ft | 4 – 8
Industrial Steel Braced Frame (1–3 story) | 25–50 ft | 0.2 – 0.6

## Slide 13
Vibrationdata
Building Period T (cont)
= Actual Fundamental Period
Approximate Code Period (ASCE 7-22 §12.8.2.1)
The period is
where
= building height (feet or meters)
= system-dependent exponent
= empirical coefficient
Structural System | Ct​ ( sec/ ftx ) | Ct​ ​ ​ ( sec/ mx ) | Exponent x
Steel Moment-Resisting Frames | 0.028 | 0.0724 | 0.8
Concrete Moment-Resisting Frames | 0.016 | 0.0466 | 0.9
Eccentrically Braced Steel Frames | 0.03 | 0.0731 | 0.75
All Other Structural Systems | 0.02 | 0.0488 | 0.75

## Slide 14
Vibrationdata
Building Period T (cont)
= Actual Fundamental Period
Approximate Code Period (ASCE 7-22 §12.8.2.1)
For moment frames:
For stiff shear wall buildings:
For very flexible tall buildings:
ASCE 7-22 allows:
Where:
= upper-bound coefficient (from table)
Typically 1.4–1.7 depending on
Mapped Value of ​ (g) | 
​≤ 0.10 | 1.7
0.10 | 1.6
0.20 | 1.5
0.30 | 1.4
0.4 | 1.3
​ ≥ 0.50 | 1.2
 | 1.7
 | 1.6
 | 1.5
 | 1.4
 | 1.3
 | 1.2

## Slide 15
Vibrationdata
Typical Building Mass Properties
Building Type | Approx. Mass per Floor Area | Approx. Mass per Floor Area | Comments
Low-rise Residential | ~40–50 psf | ~195–244 kg/m² | Light floors/finishes; low structural mass.
Office / Commercial | ~60–70 psf | ~293–342 kg/m² | Concrete slabs + partitions + furnishings.
Industrial / Warehouse | ~125 psf | ~610 kg/m² | Heavier slabs and equipment areas.
Hospital (typical floors) | ~250 psf | ~1,220 kg/m² | Hospital floor design often assumes ~1.5 kPa dead load + 4 kPa live load.
Hospital (operating room corridors) | ~80–100 psf | ~390–488 kg/m² | Operating rooms, labs & heavy corridors may have higher load requirements.
High-rise Concrete / Mixed Use | ~100–120 psf | ~488–586 kg/m² | Includes heavy structure, finishes, MEP. Typical codes vary.
The mass densities include live + dead loads
Dead loads represent the permanent weight of structural elements — slabs, beams, walls, finishes, fixed equipment, etc.
Represent variable weight from occupancy, furniture, storage, and mobile equipment

## Slide 16
Vibrationdata
Lateral Frame Stiffness
The stiffness is the lateral resistance of a floor story to horizontal displacement under wind or seismic loads
Hooke’s law, stiffness is the ratio of applied lateral force to resulting lateral drift Δ
Lateral system type (moment frame, braced frame, shear walls) strongly influences stiffness magnitude
Use simple beam/column geometry and flexural rigidity (EI) to estimate combined story stiffness
Advanced analysis: linear elastic structural finite element analysis

## Slide 17
Vibrationdata
Lumped-Mass Shear Building Model, Four Story Example, Eigenvalue Solution
Lumped-mass shear models idealize each floor as a concentrated mass connected by lateral stiffness elements
Captures the primary lateral dynamic behavior (e.g., story drifts under seismic/wind loads) without requiring fully detailed finite element meshes
Global mass & stiffness matrices
,
Generalized eigenvalue problem
where
are the eigenvalues, angular natural frequencies squared
are the eigenvectors, orthogonal mode shapes

## Slide 18
Vibrationdata
Undamped equation of motion for applied force
Great model for wind loading, but extra steps are needed for base excitation
Let be the base displacement
Define relative displacements
Lumped-Mass Shear Building Model, Four Story Example

## Slide 19
Vibrationdata
Undamped equation of motion for base excitation
Solve using modal analysis as covered in a separate unit
Lumped-Mass Shear Building Model, Four Story Example

## Slide 20
Vibrationdata
Rayleigh Method for Building Period ASCE 7-22 §12.8.2.1
where
  = seismic weight at level
  = lateral displacement at level
  = applied lateral force at level
  = 9.81 m/s² (or 386 in/s²)
  = number of levels
Procedure
Apply ASCE vertical force distribution:
Perform linear elastic static analysis → Obtain story displacements
Substitute into Rayleigh equation → Compute refined

## Slide 21
Vibrationdata
Apparent Circular Loop in ASCE 7-22
Assume building period T
Compute seismic coefficient as a function of period
Compute base shear
Distribute to get floor lateral forces
Design members → get stiffness
Compute actual T via Rayleigh energy method or Rayleigh force-displacement
Rayleigh force displacement depends on which depends on and initial assumed
Repeat if necessary
But if you know the mass & stiffness, just do the eigenvalue solution!

## Slide 22
Vibrationdata
Rayleigh Method for Building Period
where
is the fundamental mode shape with arbitrary scale
i is the story number