## Slide 1
Seismic Shock Response Spectra
Complex Oscillating Shock Pulse
Revision A

## Slide 3
Nine people were killed by the May 1940 Imperial Valley earthquake. At Imperial, 80 percent of the buildings were damaged to some degree. In the business district of Brawley, all structures were damaged, and about 50 percent had to be condemned. The shock caused 40 miles of surface faulting on the Imperial Fault, part of the San Andreas system in southern California. Total damage has been estimated at about $6 million. The magnitude was 7.1.
El Centro, Imperial Valley, Earthquake

## Slide 5
El Centro, Imperial Valley, Earthquake

## Slide 6
SDOF System Subjected to Base Excitation

## Slide 7
Algorithm
Problems with arbitrary base excitation are solved using a convolution integral
The convolution integral is represented by the Smallwood ramp invariant digital recursive filtering relationship for numerical efficiency

## Slide 8
Smallwood Digital Recursive Filtering Relationship
where Δt is the time step

## Slide 9: Relative Displacement
9
Vibrationdata
where Δt is the time step and also inverse of sample rate
Notes: 9

## Slide 12
El Centro Earthquake Exercise I
Peak Response Accel = 0.92 G

## Slide 13
El Centro Earthquake Exercise I
Peak Rel Disp = 2.8 in

## Slide 14
Pseudo Velocity
where Z is the relative displacement
is the angular natural frequency (rad/sec)
The pseudo velocity PV is
Dr. Howard Gaberson and others have written papers showing that dynamic stress is proportional to pseudo velocity

## Slide 19
El Centro Earthquake SRS

## Slide 20
El Centro Earthquake SRS

## Slide 21
El Centro Earthquake SRS

## Slide 22
El Centro NS
fn = 1.8 Hz
Accel = 0.92 G
Vel = 31 in/sec
Rel Disp = 2.8 in

## Slide 23
El Centro Earthquake SRS, Q=50, 1% damping
Assume light damping for conservatism
Highest SRS peak is 1.5 G
Add some uncertainty margin ~ 3 dB
Derive equivalent static load of 2 G
Equivalent static load derived so that civil engineers do not have to calculate natural frequency

## Slide 24
Note that current Caltrans standards require bridges to withstand an equivalent static earthquake force (EQ) of 2.0 G
May be based on El Centro SRS peak Accel + dB margin
Golden Gate Bridge

## Slide 25
Vandenberg, California SRS
NASA-HDBK-7005, Shock Response Spectrum for Typical Central California Earthquake