## Slide 1
ASCE 7-22, Ch 12, Seismic Design Requirements for Buildings
By Tom Irvine
Vibrationdata

## Slide 2
Vibrationdata
Introduction
Chapter 11 tells us how strong the earthquake is
Chapter 12 tells us what we’re allowed to build in response and controls which structural systems are legally permitted based on:
  Seismic Design Category (SDC)
  Building height
  Structural regularity
System selection is therefore a code-driven design decision, not purely an engineering preference
NEHRP Seismic Design Technical Brief No. 3, Seismic Design of Cast-in-Place Concrete Diaphragms, Chords, and Collectors

## Slide 3
Vibrationdata
Seismic Hazard Map
Each figure is based on Site Class D (the default class when the soil profile is not known) and is applicable to structures assigned to Occupancy Categories I, II, and III (buildings other than high hazard exposure structures)
Note that if the soil profile is known and is lower than D, a correspondingly lower SDC may be realized
https://www.cmha.org/resource/tek-14-18b/

## Slide 4
Vibrationdata
Seismic Hazard Map

## Slide 5
Vibrationdata
Scope
Chapter 12 = “How to design the building once hazard is known”
Applies to:
  Building Seismic Force-Resisting Systems (SFRS)
  Diaphragms
  Frames, shear walls, braced frames
  Building height & configuration limits
  Analysis procedures
  Drift and stability checks
Diagonal X-Bracing Inverted V-Bracing K-Bracing
Bracing V-Bracing
https://www.linkedin.com/pulse/bracing-up-concentric-vs-eccentric-decoding-steel-skeleton-a-j-vkbfc/

## Slide 6
Vibrationdata
Workflow
Get SDS, SD1 (Ch 11)
Determine Seismic Design Criteria (SDC)
Select structural system
Apply Ch 12 analysis & detailing rules
Corrugated Steel Floor and Roof Diaphragms with Steel cross-bracing and diagonal members for lateral stability
https://www.constructionspecifier.com/smdi-and-aisc-partner-to-establish-sdii/

## Slide 7
Vibrationdata
From Hazard to Structural System
Step | Meaning
Hazard | SS, S1, Site Class, Risk Category
SDC | A through F
System Selection | SMRF, SCBF, Shear Wall, Dual System
Analysis Method | ELF or MRSA
Drift Check | Δ ≤ Cd·Δe / Ie
Stability | P-Δ limits
Detailing | AISC 341 / ACI 318 seismic provisions
Seismic Design Category (SDC)
Equivalent Lateral Force (ELF)
Modal Response Spectrum Analysis (MRSA)
Cd = Design Deflection Amplification Factor
Ie = Importance Factor
Δe = Story Elastic Displacement
P = vertical gravity load (axial load in columns)
Δ = lateral displacement

## Slide 8
STEP 1 · Determine Risk Category (RC)
Classify by occupancy/function → RC I, II, III, or IV.
RC IV = Essential Facilities (hospitals, EOCs, fire stations)
§1.5 · Table 1.5-1
SDC B–F → Continue
Proceed to Step 4:
Select SFRS & analysis procedure
§12.2 et seq.
STEP 3 · Assign Seismic Design Category (SDC)
Use Tables 11.6-1 & 11.6-2 with SDS, SD1 and Risk Category.
Categories: A (least) → B → C → D → E → F (most severe)
§11.6 · Tables 11.6-1 & 11.6-2
SDC = A only?
§11.6 · §11.7
Apply §11.7 Only
Min. lateral force = 1% W per floor. No further seismic analysis required.
§11.7.1–11.7.3
STEP 2 · Obtain Ground Motion Parameters
Use USGS/ASCE Hazard Tool: obtain SS & S1.
Apply site coefficients: Fa, Fv per Site Class A–F.
SDS = ⅔ · Fa · SS SD1 = ⅔ · Fv · S1
§11.4.1–11.4.5 · Table 11.4-1 & 11.4-2
No
Yes
Decision Flowchart, Phase 1 – Seismic Hazard Determination

## Slide 9
STEP 4 · Select Seismic Force-Resisting System (SFRS)
Choose system from Table 12.2-1. Obtain R, Ω₀, Cd.
Verify system is permitted for assigned SDC and height limit.
Systems: Bearing Wall, Building Frame, Moment Frame, Dual,
Cantilever Column, Shear Wall–Frame Interactive
§12.2.1 · Table 12.2-1
Structural Irregularity present?
§12.3 · Tables 12.3-1 & 12.3-2
Irregularity Types (Tables 12.3-1 & 12.3-2) Horizontal & Vertical
Regular Structure
No special irregularity requirements apply.
Proceed to analysis procedure selection.
§12.3.1 — Regular structures
→ Proceed to Phase 3
Analysis Procedure Selection (§12.6)
See next slide.
Phase 2 – SFRS Selection & Structural Irregularies
Yes

## Slide 10
Vibrationdata
Phase 3 – Analysis Selection & Forces
LRHA — Reduced Roof Live Load, Horizontal Area-based
NRHA — Nominal (unreduced) Roof Live Load, Horizontal Area-based
STEP 5 · Select Analysis Procedure (Table 12.6-1)
Determine permitted method based on SDC, height h, period T, and irregularity type.
§12.6 · Table 12.6-1
ELF Procedure
Equivalent Lateral Force
V = Cs · W
Cs = SDS/(R/Ie)
Simplest method.
OK: SDC B–D, regular,
hn ≤ height limits
§12.8
Modal RSA (§12.9.1)
Multi-mode response spectrum.
Combine via SRSS or CQC.
Require ≥90% mass participation.
Required for irregular/tall.
Must scale if VMRSA < 0.85·VELF
Base shear is computed differently (summed modal forces via SRSS/CQC)
§12.9.1 · §12.9.1.4
Which Analysis Procedure?
§12.6 · Table 12.6-1
LRHA / NRHA
Linear or Nonlinear, Response History Analysis.
Permitted for all structures.
Required: isolated/damped.
Peer review required.
Base shear comes directly from the response history results, not from Cs·W
§12.9.2 · §16
ELF
MRSA
LRHA

## Slide 11
Vibrationdata
Phase 3 – Analysis Selection & Forces (cont)
STEP 6 · Compute Seismic Base Shear ELF
Cs = SDS / (R/Ie) [§12.8.1.1]
Cs,max = SD1 / (T · R/Ie) or SD1 · TL / (T² · R/Ie)
Cs,min = max(0.044·SDS·Ie, 0.01) [or 0.5·S1/(R/Ie) if S1 ≥ 0.6g]
V = Cs · W
Scale MRSA result if Vmrsa < 0.85·VELF (§12.9.1.4)
ELF
STEP 7 · Distribute Forces Vertically & Apply Torsion
Fx = Cvx · V where Cvx = wxhxᵏ / Σwihiᵏ
k = 1 (T ≤ 0.5s) | k = 2 (T ≥ 2.5s) | interpolate between
Accidental torsion: Mta = Vx · 0.05 · B (§12.8.4.2)
Amplify torsion if Type 1a/1b horizontal irregularity (§12.8.4.3)

## Slide 12
Vibrationdata
Phases 4-5, Drift, P-delta, Diaphragms & Foundations
ELF, MRSA, LRHA
STEP 8 · Compute Design Story Drift & Stability
δx = Cd · δxe / Ie (amplified elastic displacement)
Δ = δx − δx−1 (story drift)
P-Delta stability coefficient: θ = PxΔ / (Vx · hsx · Cd)
§12.8.6 · §12.8.7 · §12.12.1
Δ ≤ Δa and θ ≤ 0.10?
§12.12.1 · §12.8.7
STEP 9 · Diaphragm Forces, Collectors & Connections
Fpx = (ΣFi / Σwi) · wpx ≥ 0.2·SDS·Ie·wpx
Collector (drag strut) elements: design for Ω₀ seismic forces.
Verify diaphragm shear transfer to vertical SFRS elements.
§12.10 · §12.10.2 Collector overstrength
STEP 10 · Foundation Design & Soil–Structure Interaction
Transfer amplified seismic demands to foundation per §12.13.
SSI reduction optional per §12.13.3 (can reduce base shear).
Pile/pier detailing varies by SDC per §12.13.5.
§12.13 · Foundation detailing by SDC
Yes
No -> redesign
STEP 11 · Nonstructural Component Anchorage (§13)
Fp = 0.4·SDS·Ip·Wp · (1 + 2z/h) · (1 + 2/Rp)
Check mechanical, electrical, plumbing, cladding, equipment.
Triggered for SDC C–F. Use Tables 13.5-1 & 13.6-1.

## Slide 13
Vibrationdata
Phases 4-5, Drift, P-delta, Diaphragms & Foundations (cont)
ELF, MRSA, LRHA
FINAL COMPLIANCE CHECKLIST (All Steps Complete?)
☑ RC & SDC assigned ☑ SFRS selected from Table 12.2-1 ☑ Irregularities assessed ☑ Analysis procedure confirmed ☑ V & Fx computed
☑ Drift Δ ≤ Δa ☑ P-delta θ ≤ 0.10 ☑ Diaphragm Fpx checked ☑ Collectors: Ω₀ forces ☑ Foundation demands transferred ☑ Nonstructural anchors (§13)
SEISMIC SEPARATION GAP (§12.12.3)
Adjacent dissimilar structures:
δMT = √(δM1² + δM2²)
Same structure with joint:
δMT = δM1 + δM2 (absolute sum)
P-Delta Limits (§12.8.7): θ ≤ 0.10: No P-delta amplification needed 0.10 < θ ≤ θmax: Amplify by 1/(1−θ) θ > θmax: Redesign required

## Slide 14
Vibrationdata
Structural System Selection
R (Response Modification Factor)
  Reduces design forces → assumes ductility and energy dissipation
Ω₀ (Overstrength Factor)
  Used for collectors, chords, connections, discontinuities
Cd (Deflection Amplification Factor)
  Used to compute amplified drift for code drift checks
Height Limits Increase with Ductility
Special systems (SMRF, SCBF, Special Shear Walls, Dual Systems) are permitted in higher SDC and greater heights
https://www.skghoshassociates.com/blog/about-that-25-increase-in-diaphragm-connection-forces/

## Slide 15
Vibrationdata
Three Seismic Modification Coefficients
Factor | Used For | Physical Meaning
R | Reduces base shear | Expected ductility
Ω₀ | Amplifies forces locally | Hidden overstrength
Cd | Amplifies drift | Inelastic deformation

## Slide 16
Vibrationdata
Overstrength Factor Ω₀
Lateral Force Amplification for specific elements that remain elastic
Overstrength Factor Use
  The overstrength factor ensures that critical elements, like foundations and columns, are designed to handle amplified forces
  This way, these parts will survive before the more ductile elements, like beams, which are intended to yield first
Benefits and Trade-Offs
  The overstrength factor:
  Helps prevent sudden brittle failures
  Supports a strong-column/weak-beam design approach improves overall seismic safety

## Slide 17
Vibrationdata
Response Modification Coefficient R “Credit for Ductility”
The R factor is defined in ASCE 7-22 as the coefficient used to reduce elastic seismic forces to design-level forces
It represents the structure’s ability to:
  Yield
  Dissipate energy
  Redistribute forces
  Avoid collapse through ductile behavior
Base shear
is the base shear that would occur if the structure remained completely elastic during the design earthquake
Base shear review
V = ​W
Base shear
  If T < Ts ,
      If T > Ts ,
    Ts is the transition period between the constant-acceleration and constant-velocity regions of the design response spectrum

## Slide 18
Plastic Hinges in Beam Structures
A plastic hinge forms when a structural member reaches its plastic moment capacity and begins to rotate inelastically while maintaining near-constant moment
The Strong Column – Weak Beam (SCWB) requirement ensures Plastic hinges form in beams instead of columns
Chapter 12 requires systems that provide ductile detailing
The design philosophy is to always localize damage in ductile elements & protect gravity-load-carrying members
Image courtesy of Canterbury Earthquake Royal Commission

## Slide 19
Vibrationdata
Formation of Plastic Hinge Zone
https://seblog.strongtie.com/2024/11/framing-the-future-the-evolution-of-moment-frames/formation-of-plastic-hinge-zone/
A wide-flange steel beam framing into a column with web yielding
A plastic hinge is not a literal hinge
It is a localized region where the section has yielded across most of its depth and rotates at approximately constant bending moment
The goal is controlled energy dissipation through stable beam plastic hinging

## Slide 20
Vibrationdata
Structural Ductility
Ductility Level | Structural System | Primary Behavior | Typical R | Typical Ω₀ | Typical Cd | Design Philosophy
Low | Ordinary Shear Wall | Strength-controlled | 3 | 2.5–3 | 2.5 | Limited inelastic rotation
 | OCBF | Brace buckling governed | 3.25 | 2 | 3 | Limited ductility
 | OMF | Limited moment ductility | 3–3.5 | 3 | 3 | Basic detailing
Moderate | IMRF | Controlled yielding | 4–5 | 3 | 4 | Improved detailing
 | Special RC Shear Wall | Confined boundary yielding | 5–6 | 2.5–3 | 5 | Capacity design elements
OCBF = Ordinary Concentrically Braced Frame
OMF = Ordinary Moment Frame
IMRF = Intermediate Moment Resisting Frame

## Slide 21
Vibrationdata
Structural Ductility
Ductility Level | Structural System | Primary Behavior | Typical R | Typical Ω₀ | Typical Cd | Design Philosophy
High | SCBF | Stable brace yielding | 6 | 2 | 5 | Designed ductile fuse
 | SMRF | Plastic hinge mechanism | 8 | 3 | 5.5 | Strong-column weak-beam
 | EBF | Link beam yielding | 8 | 2 | 5 | Replaceable ductile links
 | Dual Systems | Frame + wall interaction | 7–8 | 2.5–3 | 5–6 | Redundant energy dissipation
SCBF = Special Concentrically Braced Frame
SMRF = Special Moment Resisting Frame
EBF = Eccentrically Braced Frame

## Slide 22
Vibrationdata
Permitted Analysis Procedures
Method | Use
Equivalent Lateral Force (ELF) | Most common
Modal Response Spectrum Analysis (MRSA) | Required for taller/irregular buildings
Nonlinear Response History | Chapter 16
Simplified Method | Limited low-rise
https://www.linkedin.com/posts/shawkatalikhan_the-equivalent-lateral-force-elf-procedure-activity-7363651518165663746-DMu-/

## Slide 23
Vibrationdata
Equivalent Lateral Force
Steps:
  Compute period T
  Compute Cs
  Compute base shear V = Cs W
  Distribute vertically
  Check drift
Valid for:
  Regular structures
  Limited height
  Certain SDC limits
Covered in previous slide set
https://www.youtube.com/watch?v=GjNI3VGmEfc

## Slide 24
Vibrationdata
Response Modification & Height Limits by SDC
System | R | Ω₀ | Cd | Height Limits by SDC
Steel Special Moment Frame (SMRF) | 8 | 3 | 5.5 | No explicit limit in B/C; permitted to greater heights in D/E/F (commonly up to 160 ft+ depending on SDC & occupancy)
Steel Intermediate Moment Frame (IMRF) | 4.5 | 3 | 4 | Limited in SDC D; typically not permitted in E/F for tall buildings
Steel Ordinary Moment Frame (OMF) | 3.5 | 3 | 3 | Height limited in SDC C; prohibited in D/E/F
Steel Special Concentrically Braced Frame (SCBF) | 6 | 2 | 5 | Permitted in D/E/F; moderate height limits depending on occupancy

## Slide 25
Vibrationdata
Response Modification & Height Limits by SDC
System | R | Ω₀ | Cd | Height Limits by SDC
Steel Ordinary Concentrically Braced Frame (OCBF) | 3.25 | 2 | 3.25 | Limited to low-rise in C; prohibited in D/E/F
Steel Eccentrically Braced Frame (EBF) | 8 | 2 | 4 | Permitted in D/E/F; good for mid- to high-rise
Special Reinforced Concrete Shear Wall | 6 | 2.5 | 5 | Permitted in D/E/F; height limits based on occupancy
Ordinary Reinforced Concrete Shear Wall | 5 | 2.5 | 4 | Limited in C; prohibited in D/E/F
Dual System (SMRF + Shear Wall or SCBF) | 8 | 2.5–3 | 5–5.5 | Often used for taller buildings in D/E/F

## Slide 26
Vibrationdata
Building Height Limits by SDC
SDC B / C (Low–Moderate Seismic Risk)
  Ordinary systems generally permitted
  Height limits are moderate
  Dynamic analysis often not required
  Drift usually governs before system prohibition
SDC D (High Seismic Risk)
  Ordinary braced frames → height severely limited
  Ordinary moment frames → limited or prohibited
  Special systems required for taller buildings
    Special Moment Resisting Frame (SMRF)
    Special Concentrically Braced Frame (SCBF)
    Special shear walls
    Dual systems
  Increased detailing per AISC 341 / ACI 318

## Slide 27
Vibrationdata
Permitted Analysis Procedures
SDC E / F (Very High / Near-Fault)
  Ordinary systems prohibited
    Ordinary Moment Frame (OMF)
    Ordinary Concentrically Braced Frame (OCBF)
    Ordinary shear walls
  Only Special or Dual systems permitted
  Stricter height caps apply
  Dynamic analysis commonly required
Design Decision Logic
  As SDC increases:
  Permitted ductility must increase
  Allowable height for low-ductility systems decreases
  Ordinary systems are eliminated
  Special detailing becomes mandatory

## Slide 28
Vibrationdata
Structural Irregularities
ASCE 7-22 Tables 12.3-1 (Plan) & 12.3-2 (Vertical)
  Structural irregularities trigger:
  Mandatory dynamic analysis
  Torsional amplification
  Height restrictions
  Stricter detailing requirements
ST – Stepped / Setback Tower, vertically irregular
SB – Setback Building, vertically irregular
OGS – Open Ground Story, soft story / weak story irregularity
FC – Floating Column, vertical stiffness discontinuity, often with torsional issues
R – Regular

## Slide 29
Vibrationdata
Structural Irregularities
Plan Irregularities
Torsional Irregularity
  Max story drift > 1.2 × average drift
  Indicates significant rotation due to CM–CR offset
  CM is center-of-mass, CR is center-of-rigidity
  The Center of Rigidity is the point in plan where a lateral force can be applied without causing rotation
  Requires torsional amplification factor
Extreme Torsional Irregularity
  Max drift > 1.4 × average drift
  ELF may not be permitted
  Dynamic analysis required
https://structures-explained.com/torsion-in-structures/

## Slide 30
Vibrationdata
Structural Irregularities
Vertical Irregularities
Soft Story
  Story stiffness < 70% of story above OR < 80% of average of three above
  High drift concentration risk
  Common in podium / open first-floor buildings
Weak Story
  Story strength < 80% of story above
  Collapse mechanism risk
Soft-Story Building Failure, Loma Prieta Earthquake
https://seblog.strongtie.com/

## Slide 31
Vibrationdata
https://weinsteinconstruction.com/soft-story-retrofitting/
Soft Story & Retrofit

## Slide 32
Vibrationdata
Structural Irregularities
In-Plane Discontinuity
  Sudden change in lateral-force-resisting elements
  Discontinuous shear walls / braced frames
Out-of-Plane Offset
  Vertical lateral elements not aligned between stories
  Load path interruption
Diaphragm Discontinuity
  Large openings
  Abrupt stiffness changes
  Split diaphragms
Vulnerability of Buildings With Irregularity Due to Out-of-Plane Offsets in Mexico, A. Gómez-Bernal, et al.

## Slide 33
Irregularities
Irregularity →
  Higher torsion
  Concentrated drift
  Increased P–Δ
  Analysis restrictions
  Height limitations

## Slide 34
Vibrationdata
Irregular Consequences
Irregularity | Effect | Code Consequence
Torsional | Edge drift amplification | Ax required
Soft Story | Drift concentration | Dynamic analysis
Weak Story | Collapse risk | Prohibited in high SDC
Diaphragm Discontinuity | Force redistribution | Collector design
Ax​ is the torsional amplification factor applied at a given story level x
It increases the design torsional moment when a building has torsional irregularity

## Slide 35
Vibrationdata
Irregular Code Consequence Summary
Irregularity | Analysis | Height | Amplification
Torsional | MRSA required | Limited | Ax
Extreme Torsion | ELF prohibited | Severe | Ax > 1
Soft Story | Dynamic | Restricted | Drift amplified
Weak Story | Prohibited in D/E/F | N/A | Collapse risk
Diaphragm Discontinuity | Collector Ω₀ | Limited | Redistribution
Modal Response Spectrum Analysis (MRSA)

## Slide 36
Vibrationdata
Irregularity Types
Irregularity Type | SDC Trigger | Required Action
1a / 1b (Torsional) | C, D, E, F | Apply Torsional Amplification Factor
2 (Reentrant Corner) | D, E, F | 3D Analysis & Diaphragm Force Transfer Analysis
All Horizontal | D, E, F | Increased Redundancy ρ may be required if elements are removed
Irregularity Type | SDC Trigger | Required Action
1a / 1b (Torsional) | C, D, E, F | 
2 (Reentrant Corner) | D, E, F | 3D Analysis & Diaphragm Force Transfer Analysis
All Horizontal | D, E, F | Increased Redundancy ρ may be required if elements are removed
1a Torsional Irregularity
Accidental Torsion: Must be included, typically by displacing the center of mass by 5% of the building dimension.
Applicability: Rigid or semi-rigid diaphragm
<
If present in Seismic Design Categories (SDC) C, D, E, or F, this requires the application of a torsional amplification factor ( ) to the accidental torsion moment
1b Torsional Irregularity

## Slide 37
Vibrationdata
Irregularity Types (cont)
Type 2: Reentrant Corners
  Definition: Occurs in L, T, U, or H-shaped buildings where the "projections" (the wings) are longer than 15% of the total plan dimension in that direction
  The Risk: The "inside corner" of the building becomes a stress concentration point where the two wings pull in different directions
  Type 3: Diaphragm Discontinuity
  Definition: Occurs when the floor system (the diaphragm) has large cutouts or open areas (like a massive atrium) that exceed 50% of the total gross area, or when the stiffness of the floor changes by more than 50% from one story to the next
  The Risk: The floor isn't "stiff" enough to transfer the seismic forces to the walls or frames
  Type 4: Out-of-Plane Offsets
  Definition: Occurs when there is a "jog" in the lateral force path. For example, a shear wall on the 3rd floor does not sit directly above the shear wall on the 2nd floor.
  The Risk: This creates massive "overturning" forces on the floor system that has to bridge the gap between the two walls.

## Slide 38
Vibrationdata
Torsional Amplification Factor
The torsional amplification factor is
where
  = maximum story drift at one edge
  = average drift of the two edges
Torsional irregularity exists if
Design torsional moment becomes:
where
  = story shear
  = accidental eccentricity (±5% plan dimension)

## Slide 39
Vibrationdata
https://www.linkedin.com/posts/mohdabdulmannankhan_response-spectrum-analysis-rsa-is-a-seismic-activity-7328031801552134145-Jghn/

## Slide 40
Vibrationdata
Modal Analysis
ASCE 7-22 §12.9
Required when:
  Structure is irregular
  T > limits
  SDC D, E, F and exceeds height limits
  Torsional irregularity or extreme torsion
Modal analysis better captures:
  Higher mode effects
  Irregular mass/stiffness
  Tall buildings
https://help.idecad.com/ideCAD/mode-shapes-and-modal-vibration-periods

## Slide 41
Vibrationdata
Modal Response Spectrum Analysis (MRSA)
Solves eigenvalue problem
→ natural frequencies & mode shapes
Computes modal participation factors
Extracts spectral accelerations from design spectrum
Combines modal responses (SRSS or CQC)
Square-root-of-the-sum-of-the-squares (SRSS)
Complete Quadratic Combination (CQC)
Captures higher-mode effects and torsion
Generalized eigenvalue Problem
is the global stiffness matrix
is the global mass matrix
is the eigenvalue
is the eigenvector
There is one eigenvalue and corresponding eigenvector for each degree-of-freedom
Modal base shear contribution

## Slide 42
Vibrationdata
MRSA
Image courtesy of K.T. Tse
Include sufficient modes to capture ≥ 90% mass participation
Include accidental torsion
Apply torsional amplification factor Ax when required
Use 5% damping unless otherwise justified

## Slide 43
Vibrationdata
ELF & MRSA Comparison
ELF | MRSA
Assumes dominant first mode | Includes multiple modes
Cannot capture torsion properly | Includes rotational DOF
Limited for tall buildings | Accurate for higher-mode response
Static force pattern | Dynamic modal superposition

## Slide 44
Vibrationdata
Near Fault Effects, SDC F
Located near major active faults
Large spectral accelerations (high SDS and/or SD1)
Often governed by long-period ground motion effects
Strong potential for pulse-like ground motions
Velocity Pulses (Near-Fault Directivity)
  Caused by rupture propagation toward the site
  Produces large, concentrated velocity pulse
  Energy delivered in one or two strong cycles
  Can dramatically increase displacement demand
Bluff Station, Kēkerengū Valley, Kaikoura, New Zealand earthquake 2016
https://www.tasman.govt.nz/my-region/environment/environmental-management/natural-hazards/geological-hazards/earthquake-faults

## Slide 45
Vibrationdata
Near Fault Effects, SDC F
In this earthquake radiation pattern (horizontal view), SV and SH refer to the two types of S-waves (shear waves), distinguished by their particle motion direction
SV Wave — Shear Vertical
SH Wave — Shear Horizontal
Circle with green & white quadrants is a “beachball”
Fault type (strike-slip, normal, reverse, oblique

## Slide 46
Vibrationdata
Redundancy Factor ρ
The Redundancy Factor (ρ) increases seismic design forces when a structure lacks sufficient load-path redundancy
Base shear review
V = ρ ​W
Applies primarily to: SDC D, E, F
Condition | ρ Value
Adequate redundancy | 1
Limited redundancy | 1.3
A building is redundant if:
  Multiple lateral-force-resisting elements share load
  Loss of one element does not cause disproportionate failure
  More than two lines of resistance per direction (typical threshold

## Slide 47
Vibrationdata
Structural Redundancy
https://www.facebook.com/groups/705929013755256/posts/1632814721066676/
High redundancy reinforced concrete moment frame building under construction.
Multiple moment frames in both directions provide distributed lateral load paths.
Loss or yielding of a single column or beam can be redistributed to adjacent bays.
Continuous beam-column framing supports ductile plastic hinge formation across many members.
Floor slabs act as diaphragms to transfer seismic forces to multiple frame lines.

## Slide 48
Vibrationdata
Seismic Separation Gap
To prevent pounding (structural collision) between adjacent buildings or different parts of the same building during an earthquake
Pounding can cause localized crushing, shear failure in columns, or even progressive collapse
Minimum Separation Distance ( )
Each building must be set back from the property line by a distance at least equal to its Maximum Displacement (), calculated at each floor level
  : Deflection determined by elastic analysis
  : Deflection Amplification Factor (from Table 12.2-1)
  : Importance Factor
Assessing seismic gap in adjacent RC buildings post Gorkha earthquake in Nepal, Aviral Upadhayay, et al.

## Slide 49
Vibrationdata
Seismic Separation Gap (cont)
Separation Between Adjacent Buildings ()
When two buildings are on the same property, the minimum gap () between them is determined using the Square Root of the Sum of the Squares (SRSS) of their individual displacements:
Note: This statistical combination accounts for the fact that two adjacent buildings are unlikely to reach their maximum inward peak displacement at the exact same millisecond
Absolute Sum Requirement
If the buildings are not modeled or analyzed with sufficient detail to use the SRSS method, the code generally requires the Absolute Sum of the displacements: