## Slide 1
ASCE 7-22 Ch 14 Material-Specific Seismic Design
By Tom Irvine

## Slide 2
Introduction
Role of Material Design Standards
ASCE 7 defines:
  Seismic hazard
  Design response spectra
  Base shear and lateral forces
  Structural system classification
Chapter 14 Material codes define:
  Member strength
  Ductile detailing
  Connection design
  Capacity design rules
  Special seismic requirements
  ASCE 7 determines the forces
  Material codes determine how the structure survives those forces.

## Slide 3
ASCE 7 Workflow
Symbol | Name | Definition | Used For | Typical Values
R | Response Modification Factor | Reduces elastic seismic forces to design-level forces based on expected ductile behavior | Base shear calculation V = Ve / R | 3 (low ductility) to 8 (high ductility, e.g., SMF)
Cₙ (Cd) | Deflection Amplification Factor | Amplifies elastic displacements to estimate inelastic (actual) story drifts | Drift calculations | ~2 to 5.5
Ω₀ | Overstrength Factor | Amplifies forces to account for actual strength exceeding design strength | Design of collectors, connections, foundations | ~2 to 3

## Slide 4
ASCE 7 Workflow
Determine Seismic Design Category (SDC) - Chapter 11
Select Seismic Force Resisting System (SFRS) - Table 12.2-1
Compute seismic forces - Chapter 12 or 16
Design members using material standards referenced in Chapter 14
https://www.researchgate.net/publication/329572839_Chapter_17-Seismic_Resistant_Design/figures?lo=1

## Slide 5
Scope & Integration of Chapter 14
Material | ASCE 7-22 Section | Primary Design Standards Referenced | Key Notes
Steel | 14.1 | AISC 360 (General Design) AISC 341 (Seismic Provisions) | AISC 341 governs detailing for ductile seismic systems (e.g., SMF, BRBF)
Concrete | 14.2 | ACI 318 | Includes seismic detailing requirements; special provisions for precast and non-participating elements
Masonry | 14.4 | TMS 402/602 | Covers strength design (402) and construction (602) for seismic applications
Wood | 14.5 | AWC SDPWS | Provides lateral design requirements for wind and seismic loads

## Slide 6
Vibrationdata
Seismic Hazard Map
SDC | Detailing Level
A–B | Minimal
C | Moderate
D–F | Special (strict)

## Slide 7
Steel Moment Frames (SMF / IMF / OMF)
Higher R requires higher ductility, which requires stricter detailing and connection design
https://www.linkedin.com/pulse/different-types-moment-frames-victor-dang-mrtcc/
System | R | Cd | Ω₀ | Drift Capacity | Behavior
OMF (Ordinary) | 3 | ~3 | 3 | Low (~1–2%) | Limited ductility, minimal detailing
IMF (Intermediate) | 4.5 | ~4 | 3 | Moderate (~2–3%) | Some ductility, partial seismic detailing
SMF (Special) | 8 | ~5.5 | 3 | High (≥4–6%+) | Highly ductile, extensive detailing

## Slide 8
How R, Cd, and Ω₀ Work Together
Overstrength Factor (Ω₀)
Represents real, physical reserve strength in the structure
Comes from:
  Material strength exceeding nominal values
  Strain hardening
  Redundancy / load redistribution
  Conservative design assumptions
Used selectively in design (not everywhere)
Factor | Used For | Effect on Design | Key Idea
R (Response Modification) | Force design | Reduces forces | “We allow yielding → design for lower forces”
Cd (Deflection Amplification) | Drift calculation | Increases displacements | “Actual drift is larger than elastic result”
Ω₀ (Overstrength) | Special components | Increases forces | “Some elements must resist full system strength”

## Slide 9
Overstrength
Structural System | Material | Ω₀ | Notes
Special Moment Frame (SMF) | Steel | 3.0 | Highly ductile, large reserve strength
Intermediate Moment Frame (IMF) | Steel | 3.0 | Moderate ductility
Ordinary Moment Frame (OMF) | Steel | 3.0 | Limited ductility but similar Ω₀
Special Reinforced Concrete Shear Wall | Concrete | 2.5 | Good ductility, distributed yielding
Special Reinforced Concrete Shear Wall | Concrete | 2.5 | Good ductility, distributed yielding
Special Reinforced Concrete Shear Wall | Concrete | 2.5 | Good ductility, distributed yielding
Special Reinforced Concrete Shear Wall | Concrete | 2.5 | Good ductility, distributed yielding

## Slide 10
Amplified Seismic Load & Overstrength
Amplified seismic effects for design
Combines lateral and vertical loads
The amplified seismic load effect is
  verstrength factor (system-dependent)
  eismic force from analysis (ELF or MRSA)
  esign spectral acceleration (short period)
  = Dead load
When This Equation is Used
  Anchorage of components and equipment
  Collector / drag strut design
  Connections between structural elements
  Discontinuous load paths
  Non-ductile or brittle elements
≈ Expected peak force during yielding
represents vertical ground motion effect on dead load
Why the sign can be positive or negative
During an earthquake, vertical acceleration can go:
  Upward → reduces effective gravity load
  Downward → increases effective gravity load
Case | Physical Meaning | Typical Concern
+ | Heavier structure | Strength, compression
− | Lighter structure | Uplift, overturning, anchorage
Case | Physical Meaning | Typical Concern
 | Heavier structure | Strength, compression
 | Lighter structure | Uplift, overturning, anchorage

## Slide 11
Load Amplification Notes
Design Implication
Ductile elements → designed for reduced forces (use R )
Brittle/critical elements → designed for amplified forces (use )
Even though we design using:
The structure can actually develop:

## Slide 14
Definitions
Connection detailing (MOST important)
  Weld size and quality
  Bolt configuration
  Continuity plates, doubler plates
  Prequalified connection type
Ductility capacity
  How much plastic rotation the connection can sustain
  Typical expectations:
    OMF → minimal ductility IMF → moderate ductility SMF → high ductility (large rotations)
Design philosophy
  Where yielding occurs (beam vs column vs connection)
  Strong-column / weak-beam enforcement
  Overstrength considerations

## Slide 15
Steel Moment Frames (SMF / IMF / OMF)
Ordinary OMF
  No special seismic detailing requirements
  Standard AISC 360 design
  Not intended for significant inelastic behavior
Intermediate IMF
  Moderate detailing requirements
  Some limits on member proportions and connections
  Limited plastic rotation capacity
Special SMF
  Extensive seismic detailing per AISC 341
  Strong-column / weak-beam enforced
  Strict limits on width-thickness ratios
  Lateral bracing and panel zone requirements

## Slide 16
Seismic Connection Details
https://www.wbdg.org/resources/hazard-specific-building-resilience-considerations
Welded Flange (OMF) | Welded Flange Plate (OMF, IMF, SMF) | Free Flange (OMF, IMF, SMF)
Reduced Beam Section (IMF, SMF) | Bolted End Plate (IMF, SMF) | Bolted End Flange (OMF, IMF, SMF)

## Slide 17
Prequalified Connections
Connections must be stronger than the beams they connect—so the structure yields where we want it to
Prequalified connections are experimentally validated beam-column connections used in seismic design to ensure ductile behavior and reliable performance in moment frames.
Used primarily in:
  SMF (Special Moment Frames)
  IMF (Intermediate Moment Frames)
Common Prequalified Connection Types
  RBS (Reduced Beam Section) → Beam flange is intentionally weakened to force yielding away from the column face
  Bolted End-Plate Connections → Uses bolted plates to connect beam flanges to column, enabling controlled rotation
  WUF-W (Welded Unreinforced Flange – Bolted Web) → Flanges welded, web bolted for constructability and performance

## Slide 18
Hysteresis
System Type | Hysteresis Behavior | Energy Dissipation | Seismic Performance
OMF (Ordinary) | Narrow loops | Low | Limited ductility, higher forces
IMF (Intermediate) | Moderate loops | Moderate | Balanced performance
SMF (Special) | Wide, stable loops | High | Excellent ductility, reduced force

## Slide 19
Hysteresis
Ductility vs Strength Tradeoff
  OMF (R=3): High force, limited deformation capacity
  IMF (R=5): Balanced strength and ductility
  SMF (R=8): Lower force demand, large deformation capacity
Design Philosophy
  SMF → “Deform and survive”
  OMF → “Stay elastic or fail”
  IMF → Hybrid approach

## Slide 20
Beam Geometry
In typical steel framing practice, a shear tab (single-plate shear connection) is:
Welded to the supporting member (usually a column flange or girder web)
Bolted to the supported beam web
This is the standard connection used in many moment-frame and gravity-frame buildings
Wide Flange Beam

## Slide 21
ASTM A992 Structural Steel
A992 is the dominant steel used today for wide-flange beams and columns
A992 has been Mandatory since AISC 341-02
A36 no longer permitted for seismic moment frames
A992 has better ductility for seismic design
A992’s Fy/Fu ≤ 0.85 cap ensures meaningful strain hardening before fracture — critical for ductile seismic behavior
Improved weldability compared with older steels
Controlled chemistry and toughness
Property | Value
Minimum yield strength | 50 ksi (345 MPa)
Tensile strength | 65–90 ksi
Fy/Fu ratio limit (seismic) | ≤ 0.85 (prevents over-strength)
Carbon equivalent | Controlled for weldability

## Slide 22
ASTM A992 Stress-Strain Curve, Typical
US Army Corps of Engineers EDRC TR-23-11
https://apps.dtic.mil/sti/trecms/pdf/AD1208030.pdf

## Slide 23
Capacity Design
Design philosophy
  Weak beams – Strong columns
  Strong connections
  Controlled ductile yielding
Principles
  Plastic hinges occur in predetermined locations
  Brittle failure must be prevented
  Connections stronger than members
  Gravity load path maintained after yielding
Examples
  Steel moment frames
  Concrete special moment frames
  Buckling restrained braced frames
Concrete Moment Frame, New Zealand (A. Charleson)
https://taxonomy.openquake.org/terms/moment-frame-lfm

## Slide 24
Strong Connections
Connections must be designed to remain elastic while the members they connect undergo plastic deformation
ASCE 7-22 ensures this by referencing "Pre-qualified Connections" that are tested to withstand high-rotation demands referencing AISC 358-22 for design details
These connections (e.g., RBS, bolted stiffened/unstiffened extensions) are tested to ensure ductility and prevent brittle failure in special/intermediate moment frames
RBS is Reduced Beam Section
CJP is Complete Joint Penetration (groove weld at flanges)
Image: https://www.reddit.com/r/StructuralEngineering/comments/120pc1r/prequalified_connections_for_smf_and_imf/

## Slide 25
Plastic Hinge with Reduced Beam Section (RBS)
  Purpose: To prevent brittle fracture of beam-to-column welding by forcing yielding to occur within the beam itself
  Mechanism: Flanges are reduced (often with a radius cut) in a specific area near the column, lowering the local bending strength, which causes the plastic hinge to form at that location
  Design Benefits: Creates a "strong column-weak beam" scenario
  The beam develops large rotational capacity and ductility, absorbing significant energy during seismic events
  Performance: Proper design allows the connection to withstand significant story drifts (e.g., >8%) without severe strength loss
  Image: https://www.facebook.com/groups/1646963768885734/posts/1965751330340308/
Weaker section forms plastic hinge before the brittle failure of the beam-column connection

## Slide 26
Strong Column / Weak Beam
For seismic moment frames, the strong-column requirement is typically written as
where
  = column plastic moment capacity
  = beam plastic moment capacity
These are moments at the beam-column joint
ASCE 7-22 & AISC 341 require that the sum of column moment capacities exceeds the sum of beam moments capacities at a joint (typically by a factor of 6/5 or 1.2)
This forces damage into the horizontal beams rather than the vertical columns.
A beam failure is local, but a column failure can lead to progressive, global collapse
Flexural strength is maximum bending moment that a member section can resist

## Slide 27
Plastic Moment Capacity
Symbol | Meaning | English | Metric
 | plastic moment capacity | Kip-in or kip-ft | kN-m
 | steel yield stress | ksi | MPa
 | plastic section modulus | in^3 | m^3
Symbol | Meaning | English | Metric
 | plastic moment capacity | Kip-in or kip-ft | kN-m
 | steel yield stress | ksi | MPa
 | plastic section modulus | in^3 | m^3
Section Type | How is obtained
Wide-flange beams | AISC Steel Manual tables
Box sections | Section formulas
Built-up sections | Calculated from area distribution
Section Type | 
Wide-flange beams | AISC Steel Manual tables
Box sections | Section formulas
Built-up sections | Calculated from area distribution

## Slide 28
Plastic Section Modulus
The Plastic Section Modulus is calculated based on the Plastic Neutral Axis (PNA)
The PNA is the line that divides the cross-section into two equal areas
For symmetrical shapes (like an I-beam or a rectangle), the PNA is the same as the Centroidal Axis
For asymmetrical shapes, find the line where
The Plastic Section Modulus is the sum of the first moments of the areas above and below that axis
where
    is the distance from the PNA to the centroid of the top area
    is the distance from the PNA to the centroid of the bottom area
Think of as the "brute force" capacity of the beam
It assumes the material is being pushed to its absolute limit across the entire face, not just the outer edges

## Slide 29
Simple Plastic Hinge Model
Ancient
https://www.codecogs.com/library/engineering/materials/plastic-theory-of-bending.php

## Slide 30
Beam Bending, Plastic State
Mild Steel Structures do not fail when the edge Stress of any cross section reaches the Yield point
They will continue to withstand the load as long as the central core of the section remains within the Elastic State

## Slide 31
Reinforced Concrete
ACI 318 governs the design and detailing of reinforced concrete structures, focusing on member strength and ductile detailing
To ensure a structure survives seismic forces, specific requirements for "Special" systems are implemented to prevent brittle failure
Feature | Seismic Requirement | Purpose
Hoop Spacing | Strictly limited (e.g., d/4) at member ends | Prevents longitudinal bar buckling and provides core confinement
Joint Detailing | Continuous reinforcement through the beam-column joint | Maintains the integrity of the gravity load path after yielding
Shear Strength | Vn must exceed shear associated with plastic moments | Ensures a ductile flexural failure occurs before a brittle shear failure

## Slide 32
https://www.facebook.com/61572977583535/posts/standard-hook-length-for-stirrups-ties-and-hoops-a-code-based-reference-used-in-/122176548812765919/
Reinforced Concrete

## Slide 33
Hoops
  Provide lateral confinement to concrete core
  Prevent buckling of vertical bars
  Improve ductility and energy dissipation
Ends of hoops use seismic hooks (usually 135° hooks with extensions)
Hoops do not need to be welded — they work by confinement, not by rigid connection
Hooked anchorage bars ensure that reinforcement is fully developed and anchored into the footing, preventing pullout and enabling reliable force transfer—especially critical in high-moment and seismic regions
Small wire ties hold everything in place before concrete is poured
https://www.instagram.com/p/DWMe6eUFsik/

## Slide 34
Failure Modes in Seismic Design
Desired (Ductile Behavior) | Undesired (Brittle Behavior)
Beam flexural yielding | Column failure
Distributed plastic hinges | Single-story (soft-story) mechanism
Concrete confined crushing | Shear failure (sudden, brittle)
Stable hysteresis (energy dissipation) | Fracture / connection rupture
Ductile behavior provides warning and energy dissipation
Brittle behavior leads to sudden, catastrophic collapse
Capacity design ensures yielding occurs in controlled locations
“Strong-column / weak-beam” prevents global instability

## Slide 35
Unreinforced joints fail in brittle shear, with diagonal cracking and concrete crushing
Lack of confinement = weak link, causing joint failure before beams can yield
Closely spaced hoops (ties) confine the joint, increasing strength and ductility
Ties improve bond and shear transfer, enabling a truss-like load path in the joint core
Proper detailing leads to ductile behavior, with higher load capacity and energy dissipation
Supports capacity design philosophy: strong column–joint, weak beam (controlled plastic hinging)
https://www.instagram.com/p/DWB7D7XDX37/

## Slide 36
References
Material System | Primary Design Standard | Description | Reference Link
Reinforced Concrete | ACI 318 – Building Code Requirements for Structural Concrete | Governs design and detailing of reinforced and prestressed concrete structures. Includes seismic design provisions such as special moment frames, shear walls, and confinement reinforcement. | American Concrete Institute — https://www.concrete.org
Structural Steel | AISC 360 – Specification for Structural Steel Buildings | General steel design provisions including member strength, stability, and connection design. | American Institute of Steel Construction — https://www.aisc.org
 | AISC 341 – Seismic Provisions for Structural Steel Buildings | Provides seismic detailing requirements for steel moment frames, braced frames, and other seismic systems. | American Institute of Steel Construction — https://www.aisc.org

## Slide 37
References
Material System | Primary Design Standard | Description | Reference Link
Composite Steel–Concrete | AISC 360 / AISC 341 | Governs composite structural systems where steel and concrete act together, including composite beams, columns, and moment frames with seismic detailing provisions. | American Institute of Steel Construction — https://www.aisc.org
Cold-Formed Steel | AISI S400 – Seismic Design Standard for Cold-Formed Steel Structural Systems | Provides seismic design requirements for cold-formed steel lateral force-resisting systems including shear walls, strap-braced walls, and diaphragms. | Steel Framing Industry Association — https://www.cfsei.org

## Slide 38
References
Material System | Primary Design Standard | Description | Reference Link
Wood Structures | NDS – National Design Specification for Wood Construction | Governs design of wood structural members and connections. Seismic provisions are used in conjunction with special detailing for shear walls and diaphragms. | American Wood Council — https://www.awc.org
Masonry | TMS 402 / TMS 602 – Building Code Requirements and Specification for Masonry Structures | Covers design and construction requirements for reinforced and unreinforced masonry including seismic detailing of masonry shear walls and reinforced masonry elements. | The Masonry Society — https://www.masonrysociety.org
Aluminum Structures | Aluminum Design Manual (ADM) | Provides design requirements for aluminum structural members and connections including strength, stability, and serviceability considerations. | The Aluminum Association — https://www.aluminum.org