## Slide 1
Force Limiting & PSD Notching for Shaker Tests
Revision B
By Tom Irvine

## Slide 2
PSD Shaker Tests, Over-Test Concern, Notching
Avionics components and some spacecraft are subjected to PSD base input tests to verify their design, workmanship and ability to withstand the maximum predicted random vibration environment
The components are mounted to shelves, bulkheads, panels and brackets in the launch vehicle
Spacecraft are mounted on adapter cones or dispensers
These mounting structures have less mechanical impedance than the rather rigid vibration test fixtures
A concern is that high test fixture impedance will cause an over-test at the natural frequencies of the test item
The base input PSD may be notched to prevent this over-test
mechanical impedance = force / velocity
is a function of frequency

## Slide 3
Payload Adapter & Test Fixture
This is analogous to attaching a flexible structure to a rigid wall → force amplification occurs at resonance
Typical flexible payload adapter
Payload mounted via rigid fixture to shaker table

## Slide 4
NASA GEVS
NASA GEVS requires correcting shaker-to-flight impedance mismatch
GEVS allows two primary corrections:
  1. Mass Loading (Add Mass)
    Add physical mass to:
      test fixture
      mounting interface
    Goal:
      make lab impedance closer to flight system
  2. Force Limiting (Preferred Modern Method)
    Do not change hardware, instead:
      limit force using:
        load cells (dual control), or
        computed limits (accel-only method)

## Slide 5
Goals
Prevent interface force over-test
Protect:
  Mounting brackets
  Bolted joints
  Electronics cards
  Failure modes:
    Fastener yield
    PCB cracking
    Connector damage
Key statement: Acceleration is the input — force is what breaks hardware

## Slide 6
Force vs. Acceleration
Acceleration alone is misleading
Same acceleration → different force if mass changes
Resonance → effective mass increases
Rigid fixture → artificially high force
Visual idea:
  Two systems:
    flight (flexible)
    lab (rigid)
Same acceleration PSD → different force

## Slide 7
Apparent Mass, Frequency Response Function, Magnitude
The apparent mass is the force divided by acceleration
and are complex
Below resonance: structure behaves as rigid mass
Above resonance: apparent mass decreases due to modal effects
Measurement of the frequency response function is preferred over analysis, since damping is difficult to estimate and model

## Slide 8
Apparent Mass Example
K1
K2
ma,1
ma,2
m3
m2
x3
x2
x1
m1
Consider the three degree-of-freedom model
The apparent mass is taken as the transmitted force through spring K1 divided by the m1 acceleration
The transmitted force is approximate given that modal damping is commonly used, and there is no exact method to convert modal damping into discrete dashpots
Shaker table
Test item

## Slide 9
Variables
= Force Power Spectral Density Unnotched
  Units: or
  Represents the predicted interface force spectrum between shaker and test item.
= Force Limiting Constant (or Coupling Factor)
  Dimensionless
  Semi-empirical factor that accounts for:
    Modal participation
    Boundary conditions
    Test article dynamics
  Typical values: ~0.5 to 2 (often ~1 as a starting point)
= Effective (or Modal) Mass
  Units: lbm or kg
  Represents the participating mass at the interface for the mode of interest
  Not necessarily total mass — often modal or apparent mass
= Acceleration Power Spectral Density
  Units: or
  This is the input acceleration spectrum from the shaker

## Slide 10
Apparent & Effective Mass
Feature | Apparent Mass (​) | Effective Modal Mass ()
Definition | The ratio of the transmitted force to the input acceleration. Dynamic (frequency dependent)’ “How much mass the shaker feels at that frequency.” | The portion of the total mass that participates in a specific vibration mode. Static participation. “How much mass participates in the mode.”
Frequency Dependence | Varies with frequency; acts as a rigid mass below resonance and decreases above it | Typically treated as a static value for a specific mode or lumped local mass
Primary Use | Used to calculate the "unnotched" force that a rigid shaker would apply | Used in the semi-empirical formula to define the safe force limit
How it is Determined | Best measured via FRF (Frequency Response Function) since damping is hard to model | Often estimated as 50–100% of the local static mass or derived from FEA
Mathematical Relation |  | is a component used to approximate near resonance
Feature |  | 
Definition | The ratio of the transmitted force to the input acceleration. Dynamic (frequency dependent)’ “How much mass the shaker feels at that frequency.” | The portion of the total mass that participates in a specific vibration mode. Static participation. “How much mass participates in the mode.”
Frequency Dependence | Varies with frequency; acts as a rigid mass below resonance and decreases above it | Typically treated as a static value for a specific mode or lumped local mass
Primary Use | Used to calculate the "unnotched" force that a rigid shaker would apply | 
How it is Determined | Best measured via FRF (Frequency Response Function) since damping is hard to model | Often estimated as 50–100% of the local static mass or derived from FEA
Mathematical Relation |  | 

## Slide 11
Forcing Limiting Constant C
Interface Type | Recommended C2 | Rationale
Circular Ring / Bolted Circle | 1.25 – 1.5 | High symmetry and uniform load distribution
Rectangular Plate / Bulkhead | 2.0 | Standard NASA baseline for general components
Flexible Brackets / Standoffs | 3.0 – 5.0 | Low local impedance; higher force allowed before notching
Complex/Large Assemblies | < 1.0 | Requires specific "Apparent Mass" measurements or flight data

## Slide 12
Modal Effective Mass
The effective modal mass is
The participation factor is
where
is the eigenvector for mode
is the mass matrix
is the influence vector
Computed from mode shapes and mass matrix
Includes contribution from all participating modes
Avoids arbitrary assumptions (e.g., “50–100% of mass”)

## Slide 13
Force PSD Unnotched
is the theoretical force measured at the interface if the shaker maintains the full, nominal acceleration specification regardless of the specimen's resonance
It is calculated by multiplying the input acceleration by the square of the Apparent Mass
At resonance, the apparent mass is very high, causing to show large peaks that often exceed structural design limits
=

## Slide 14
Force Limiting Equation
The requirement for mass-tailoring in specifications like NASA GEVS arises from the need to correct the Mechanical Impedance mismatch between rigid laboratory shakers and flexible flight structures
By implementing Force Limiting, test engineers can prevent over-testing at resonance frequencies
Predict a force limit using the semi-empirical formula from NASA-HDBK-7004C
The Force Power Spectral Density Limit is
Take as the total static mass for a conservatively high force limit, or use the effective mass for realism
Measure interface forces using Force
Using a dual-control vibration system to notch the acceleration input when the force limit is reached

## Slide 15
Refined Force Limiting Equation
The Force Power Spectral Density Limit is
where is the excitation frequency and is the natural frequency

## Slide 16
Notched Acceleration PSD
The resulting notched acceleration specification is
This is the result of a force-limited test, not the input for a standard, accelerometer-only test
In a real force limited vibration test, the shaker controller monitors both acceleration and force in real-time
The controller only "notches" (drops the power) when the measured force actually hits the
An accelerometer-only test is risky due to potential shifts of the test natural frequencies relative to the analytical ones, which may result in either over or under-tests at certain frequencies

## Slide 17
Notched Acceleration PSD (cont)
Raw notched PSD may contain:
  sharp corners
  narrow dips
These can:
  destabilize shaker control
  be difficult to implement
Apply smoothing in log-frequency domain
Re-enforce:
  acceleration limit
  force limit
This step is not in NASA explicitly, but it is absolutely required for a real test specification
After smooth, ensure

## Slide 18
Typical Values from NASA-HDBK-7005
Parameter | Typical Range
 | 0.7 – 1.5
 | 50–100% of local mass
Notch depth | 3–12 dB
Parameter | Typical Range
 | 0.7 – 1.5
 | 50–100% of local mass
Notch depth | 3–12 dB
“how much mass participates in the mode”
“how much mass the shaker feels at that frequency”
Recall that the apparent mass is the force divided by acceleration
The two mass parameters are related by
where is the viscous damping ratio and
This relationship is approximate near dominant modes

## Slide 19
Test Strategies
Feature | Dual Control (Force + Accel) | Accelerometer-Only
Accuracy | High; measures real-time force | Moderate; based on estimates
Complexity | High; requires load cells and extra cables | Low; uses standard test setup
Risk | Accurate but sensors can fail | Higher risk of over-test if is wrong. Measured and analytical natural frequencies may differ.
Feature | Dual Control (Force + Accel) | Accelerometer-Only
Accuracy | High; measures real-time force | Moderate; based on estimates
Complexity | High; requires load cells and extra cables | Low; uses standard test setup
Risk | Accurate but sensors can fail | 

## Slide 20
Dual Control Strategy, Force Transducers + Accelerometers
The Mars exploration Rover “Opportunity” during an FLVT test. Eight 3-component force sensors (Type 9067C) were used
https://www.aerospacetestinginternational.com/news/acoustic-vibration/how-to-test-satellites-and-not-destroy-them.html

## Slide 21
Dual Control Strategy, Force Transducers + Accelerometers
Primary Control: Acceleration is maintained at the specified profile
Limiting Control: Force transducers (load cells) measure the interface force
Low-Level Signature Sweeps: Use a 0.25 G or 0.5 G "signature" random run to verify the force limiting control settings before proceeding to Full Level (100%) testing
Notching: If the measured force sum reaches the predicted limit, the vibration controller automatically "notches" (reduces) the acceleration input to ensure the force limit is not exceeded

## Slide 22
Dual Control Strategy, Force Transducers + Accelerometers
Preloading: The bolts passing through the sensors are tightened to a specific "preload" value
This allows the sensors to measure both compression (when the shaker pushes up) and tension (when the shaker pulls down or the test article's momentum pulls away)
Summation: The individual signals from each of the force sensors are sent to a summing junction or a digital controller
By adding the vertical Z-axis signals together, the total axial force is calculated
By comparing the differences between the sensors, the overturning moments () can also be monitored
Dual Control: The vibration controller monitors both the base acceleration (via accelerometers) and this summed force
If the force reaches the defined limit , the controller automatically "notches" (reduces) the drive voltage to ensure the force never exceeds the hardware's design limit

## Slide 23
Accelerometer-only Force Limiting Control Strategy
When force transducers cannot be used, PSD Notching (or response limiting) is employed
This involves predicting the response at critical locations and manually or automatically reducing the input PSD to ensure these responses do not exceed safety limits
Manual Notching: Pre-calculated based on Finite Element Analysis (FEA)
Automatic Notching: The controller monitors an accelerometer at a critical internal component and reduces the drive signal if a pre-set GRMS or spectral limit is reached

## Slide 24
Accelerometer-only Force Limiting Control Strategy (cont)
Force can be estimated using apparent mass when it is not measured directly per NASA-HDBK-7004C
Implication for PSD
Converts acceleration PSD → force PSD
Without force sensors, apparent mass is no longer measured and must be
      Estimated from FEM
      Approximated as % of total mass
      Taken from prior test data
  Frequency dependence is critical:
    Flat assumption → risky
    Mode-specific → better

## Slide 25
Accelerometer-only Force Limiting Control Strategy (cont)
Start from Force PSD relation
Indirect notching
is the lumped local or modal mass
is a coupling factor
Rearrange to get allowable acceleration

## Slide 26
Accelerometer-only Force Limiting Control Strategy (cont)
Estimate
  Modal or local mass,
  Coupling factor, 0.7–1.5
Compute force limit from NASA-HDBK-7004 or similar
Modify input PSD
  Apply notches at resonances
Add safety margin:
  Reduce PSD by 3–6 dB near resonances
Run Test
  Single control loop (acceleration only)

## Slide 27
Force Limiting Example
The following example is loosely based on the NASA JPL SMAP Satellite, Vertical Axis Test
Model the spacecraft as a two-degree-of-freedom system attached to a shaker mass
The Delta II base input qualification PSD is the baseline shaker specification and is modified for force limited vibration testing

## Slide 28
Force Limiting Example

## Slide 29
Force Limiting Example

## Slide 30
Three dof System

## Slide 35
Three dof System, Apparent Mass

## Slide 38
Three dof System
The Unnotched Force PSD () represents the interface force that would be generated if the shaker table (the launch vehicle) were infinitely stiff. In practice, it is used as the baseline for Force Limited Vibration (FLV) testing to prevent over-testing the spacecraft at its resonant frequencies

## Slide 39
Three dof System

## Slide 40
Three dof System

## Slide 41
Three dof System
K1
K2
ma,1
ma,2
m3
m2
x3
x2
x1
m1
Shaker table
Test item

## Slide 42
MIL-STD-810H
Force control is a recognized control strategy.
  Method 514.8 paragraph 4.2.1.2 establishes force control as one of five explicitly defined control strategies (alongside acceleration input, acceleration limit, acceleration response, and waveform control), giving it formal standing in the standard
Impedance mismatch is the key driver
  Where impedance mismatch between platform/materiel and laboratory vibration exciter/test item are significantly different, force control or acceleration limiting control strategies may be required to avoid unrealistically severe vibration response
Field data must justify any force limiting. The use of control limits should be based upon field data measurements and the sensitivity of the materiel to excessive vibratory loading (e.g., a resonance condition).

## Slide 43
MIL-STD-810H (cont)
is covered in the engineering annex
  Annex A, Section 2.4.1 specifically addresses mechanical impedance as part of the platform/materiel and fixture/test item interaction discussion — providing the technical background underlying why force limiting is needed
The standard is permissive, not prescriptive
  MIL-STD-810H acknowledges force limiting as appropriate and provides the framework to use it, but does not specify how to derive force limits
  For that methodology, practitioners are directed to NASA-HDBK-7004C, which provides the semi-empirical and other derivation methods