## Slide 1
Vibrationdata
Multi-degree-of-freedom System
Shock Response Spectrum
Revision D

## Slide 2
The Shock Response Spectrum (SRS) can be extended to multi-degree-of-freedom systems
There are two options each requires a starting normal modes analysis
  Modal transient analysis using synthesized waveform
  Approximation techniques using participation factors and normal modes (modal combination methods)
The second method is called Modal Response Spectrum Analysis (MRSA) in earthquake engineering
It is a dynamic analysis method used in seismic design, including procedures referenced in ASCE 7-22 Chapter 12
Both method assume linearity
Vibrationdata
Introduction

## Slide 3
Vibrationdata
Two-dof System Subjected to Base Excitation
Damping will be applied as modal damping

## Slide 4
m2
k2 (x2-x1)
x2
x1
m1
k1 ( x1 - y )
k2 ( x2 - x1 )
Free-Body Diagrams

## Slide 5
Assemble the equations in matrix form
The equations are coupled via the stiffness matrix
Vibrationdata
Global Equations of Motion

## Slide 6
Vibrationdata
Relative Displacement Substitution
Define relative displacement terms as follows
The resulting equation of motion is
This works for some simple systems. Enforced acceleration method is required for other systems.

## Slide 7
Vibrationdata
General Form
where

## Slide 8
Vibrationdata
Decoupling
Decouple equation of motion using eigenvalues and eigenvectors
The natural frequencies are calculated from the eigenvalues
The eigenvectors are the “orthogonal normal modes”
Details given in accompanying reference papers

## Slide 9
Vibrationdata
Proposed Solution
Homogeneous problem:
Seek a harmonic solution for the homogeneous (free vibration) problem of the form
ω = the angular natural frequency (rad/sec)
= modal coordinate vector or eigenvector
where

## Slide 10
Vibrationdata
Solution Development
The solution and its derivatives are
Substitute into the homogeneous equation of motion

## Slide 11
Vibrationdata
Generalized Eigenvalue Problem
Eigenvalues are calculated via
K is the global stiffness matrix
M is the global mass matrix
ω is the angular natural frequency (rad/sec)
where
There is a natural frequency for each degree-of-freedom

## Slide 12: Solve for Eigenvalues
Vibrationdata
Find the eigenvalues by setting the determinant equal to zero
The roots ω12 and ω22 are the squares of the angular natural frequencies (rad/sec)
Polynomial solutions are available for up to 4-dof systems
Numerical methods are used for higher dof systems

## Slide 13
Vibrationdata
Generalized Eigenvalue Problem (cont)
Calculate eigenvectors
The eigenvectors describe the relative displacements of the degrees-of-freedom for each mode
The overall motion of the system is a superposition of the individual modes for the case of free vibration (aka modal superposition)
There is a corresponding mode shape for each natural frequency

## Slide 14
Vibrationdata
Eigenvector Relationship
(identity matrix)
(diagonal matrix of eigenvalues)
Form matrix from eigenvectors
Each eigenvector has an arbitrary scale factor
But mass-normalize the eigenvectors such that
Then
Column 1 is mode 1
Column 2 is mode 2
Row 1 is dof 1
Row 2 is dof 2

## Slide 15
Vibrationdata
Decouple Equation of Motion
Coupled equation of motion
Define a modal displacement coordinate
Substitute into the equation of motion
Premultiply by
Orthogonality relationships yields

## Slide 16
Vibrationdata
Modal Equations of Motion
The equation of motion becomes
Now add damping matrix
is the modal damping for mode i

## Slide 17
Vibrationdata
Candidate Methods, Time Domain
Runge-Kutta - becomes numerically unstable for “stiff” systems
Newmark-Beta - reasonably good – favorite of Structural Dynamics textbooks
Digital recursive filtering relationship - best choice but requires constant time step

## Slide 18
Vibrationdata
Participation Factors
Participation factors and effective modal mass values can be calculated from the eigenvectors and mass matrix
These factors represent how “excitable” each mode is for base excitation
Please read:
https://blog.vibrationdata.com/2026/02/07/effective-modal-mass-and-modal-participation-factors/

## Slide 19
Vibrationdata
Participation Factors for Example
is the participation factor for mode i
+ =
For the two-dof example in this unit

## Slide 24
Q=10 is the same as 5% damping

## Slide 29
MDOF Estimation for SRS, Modal Combination Methods
Method | Description | Application
ABSSUM | absolute sum method | Highly conservative upper-bound combination
SRSS | square-root-of-the-sum-of-the-squares | Standard for systems with well-separated modal frequencies (Δf/f > 0.2). Appropriate for simple, lightly coupled MDOF structures.
CQC | Complete Quadratic Combination | Preferred for closely spaced modal frequencies or moderate damping (ξ ≈ 0.02–0.10). Recommended by ASCE 7 and IEEE 344 for seismic or dynamic response analyses.
NRL | Naval Research Laboratory method | Used in shock qualification standards (e.g., MIL-STD-810H, MIL-STD-1540). Suitable when empirical data or coupling information is available for transient or SRS testing.

## Slide 30
Vibrationdata
ABSSUM Method
Pick D values directly from Relative Displacement SRS curve for mode j’s natural frequency
Conservative assumption that all modal peaks may occur simultaneously
Let be the maximum relative displacement for coordinate or dof i
Where is the mass-normalized eigenvector coefficient for coordinate i and mode j
is the participation factor for mode j
These equations are valid for relative displacement, pseudo velocity and absolute acceleration
=

## Slide 31
Vibrationdata
SRSS Method
These equations are valid for relative displacement, pseudo velocity and absolute acceleration
Pick D values directly off of Relative Displacement SRS curve

## Slide 32
Vibrationdata
CQC Method

## Slide 33
Vibrationdata
CQC Method (cont)

## Slide 34
Vibrationdata
CQC Method (cont)
The CQC (Complete Quadratic Combination) method can yield results slightly greater than the ABSSUM (absolute sum) method for very closely spaced modes, although this is rare and limited to extreme correlation cases

## Slide 35
Vibrationdata
Example: 4-dof Shear Building Model
5% damping for all modes
Perform normal modes analysis
k2
k3
k4
ma,1
ma,2
m3
m2
m1
k1
x3
x2
x1
m4
x4
ӱ
Story | Mass (lbm) | Stiffness (lbf/in) | Height (ft)
1 | 1.6e6 | 3.5e6 | 15
2 | 1.6e6 | 3.2e6 | 30
3 | 1.6e6 | 2.8e6 | 45
4 | 1.4e6 | 2.4e6 | 60

## Slide 53: Story Drift Comparison
Story | MRSA CQC Drift (%) | Modal Transient Drift (%)
1 | 0 | 0
2 | 0.656 | 0.654
3 | 0.555 | 0.558
4 | 0.332 | 0.335
Excellent agreement
Parseval’s theorem explains why: modal energy computed in frequency-domain methods can match the full time-domain transient response

## Slide 54
SRS Specification Q Concerns
The shock response of a physical coordinate in a multiple-degree-of-freedom system can be approximated as the summation response of a series of single-degree-of-freedom systems (modal superposition)
This method works best if the specification SRS has the same Q as the component’s modes
The goal is to use modal combination methods to avoid computation time for a full modal transient analysis
For example, the specification is typically Q=10 but the structure may have modes with Q=20
The higher Q yields a higher SRS, but there is no exact direct scaling method
Use conservative approach loosely based on Miles’ equation

## Slide 55
Miles Equation for Base Input PSD Applied to Response Spectrum (RS)
The SDOF system overall response acceleration to a base input PSD is
Assumes PSD is constant from 0 to infinity Hz
Can be used if PSD is constant within ± one octave of natural frequency
Miles’ equation can either over or under-predict GRMS response otherwise
where
fn = natural frequency
P = PSD level at fn
Q = amplification factor
Make the conservative assumption that
where >
Note that