## Slide 1
Launch Vehicle Static Fire
Explosion Fault Tree Analysis
Generic Liquid-Propellant Launch Vehicle
First-Stage Engine Static Fire — Pre-Flight Stand Test
Top Event: Vehicle Destruction Shortly After Engine Ignition
Tom Irvine | Vibrationdata
Fault tree structured per MIL-STD-882E / NASA SP-2010-580 logic

## Slide 2
Acronyms & Abbreviations
Vibrationdata
AIAA
American Institute of Aeronautics and Astronautics
BLEVE
Boiling Liquid Expanding Vapor Explosion
COPV
Composite Overwrap Pressure Vessel
CRS
Commercial Resupply Services (SpaceX/NASA ISS missions)
EMI
Electromagnetic Interference
FAA
Federal Aviation Administration
FOD
Foreign Object Damage / Debris
FTS
Flight Termination System
GSE
Ground Support Equipment
He
Helium (pressurant gas)
IFT
Integrated Flight Test (Starship)
ISS
International Space Station
LC
Launch Complex
LH₂
Liquid Hydrogen
LLIS
Lessons Learned Information System (NASA)
LOX
Liquid Oxygen
LV
Launch Vehicle
MIL-STD
Military Standard
MSFC
Marshall Space Flight Center
NASA
National Aeronautics and Space Administration
NASA-STD
NASA Technical Standard
NDT
Non-Destructive Testing / Inspection
RP-1
Rocket Propellant-1 (highly refined kerosene)
RCS
Reaction Control System
RSO
Range Safety Officer
SDOF
Single Degree of Freedom
S/N
Serial Number
SP
Special Publication (NASA document series)
SSC
Stennis Space Center
V&V
Verification and Validation
Author: Tom Irvine | Vibrationdata

## Slide 3
Scenario Definition & Fault Tree Assumptions
Vibrationdata
SCENARIO
Vehicle type
Generic orbital-class liquid-propellant LV
Propellants
Cryogenic oxidizer (LOX) + liquid fuel (RP-1 or LH₂)
Configuration
Mounted vertically on launch stand, umbilicals connected
Test objective
Static fire: full-duration or acceptance burn of stage 1
Engine history
Each engine individually acceptance-tested prior to integration
Failure event
Vehicle explosion shortly after engine ignition command
FAULT TREE ASSUMPTIONS
Vehicle is fully fueled at ignition command
Normal ignition sequence was commanded
Explosion = rapid uncontrolled release of chemical energy
Both BLEVE and detonation mechanisms are considered
Stand hardware, GSE, and facility are potential causes
Human factors included as basic events
Each engine has prior hot-fire history from acceptance tests
Accumulated thermal/fatigue damage is a latent risk factor
Analysis covers T-0 ignition command to T+5 seconds
Author: Tom Irvine | Vibrationdata

## Slide 4
Fault Tree — Top Event & Level-1 Branches
Vibrationdata
OR gate: any single branch is sufficient to cause vehicle destruction
TOP EVENT
Vehicle Destruction at Static Fire
OR
PROPELLANT
SYSTEM
ENGINE /
COMBUSTION
STRUCTURAL
CONTROL /
AVIONICS
GSE /
HUMAN ERROR
ACCUMULATED
FATIGUE
Propellant leak
Relief valve failure
Propellant mixing
Tank overpressure
Check valve back-flow
Hard start
Combustion instability
Turbopump failure
Injector damage
Nozzle liner burn-through
Airframe overpressure
Stand attach failure
Thermal overload
Pre-existing crack
Explosive bolt misfire
Shutdown cmd failure
Ignition sequencer error
Sensor false-nominal
Abort system inhibit
Software logic fault
Umbilical disconnect fail
Loading error
Procedure deviation
GSE valve wrong state
Range safety fault
Turbopump bearing wear
Combustion liner fatigue
Injector face cracking
Flex line fatigue
Assembly damage
Each Level-1 branch connects through an OR gate — see subsequent slides for detailed sub-trees
Author: Tom Irvine | Vibrationdata

## Slide 5
Branch 1 — Propellant System Failure (Detailed Sub-Tree)
Vibrationdata
Liquid propellant systems are the most common source of catastrophic failure in static fire events
PROPELLANT SYSTEM FAILURE (OR)
LEAK /
RUPTURE (OR)
Propellant line crack (fatigue/mfg defect)
Fitting or flange seal failure
Flexible bellows rupture
Weld defect in tank or feedline
FOD damage to line
Thermal cycling embrittlement (LH₂)
OVER-
PRESSURE (OR)
Relief valve fails closed
Pressurant regulator runaway
Rapid chill-down pressure spike
Water hammer (valve slam)
He pressurant over-drive
Tank vent valve fails closed
PROPELLANT
MIXING (OR)
Oxidizer / fuel contact outside engine
Cross-connection of fill lines
Leaking common bulkhead
Spilled propellant on hot surface
LOX-enriched atmosphere + ignition
Ullage gas contamination
LOADING /
PURGE ERROR (OR)
Wrong propellant loaded (contamination)
Incomplete purge — residual air in LOX line
Fill level sensor failure
Ground loading valve left open
Chill-down sequence skipped
Boiloff vent blockage
■ = Basic event (lowest-level failure) All sub-branches connected by OR gate to parent
Author: Tom Irvine | Vibrationdata

## Slide 6
Branch 2 — Engine / Combustion Failure (Detailed Sub-Tree)
Vibrationdata
Hard starts, combustion instability, and nozzle liner burn-through are leading engine failure modes
ENGINE / COMBUSTION FAILURE (OR)
HARD START (OR)
Excess propellant in chamber pre-ignition
Igniter fires late / out of sequence
Fuel-rich or oxid-rich slug ignites
Main valve opens before igniter confirms
Chamber pressure spike exceeds limit
Ignition sequence timing error
COMBUSTION
INSTABILITY (OR)
High-frequency acoustic instability
Low-frequency chugging
Injector element damage / asymmetry
Combustion coupled to structural mode
Inadequate baffles / dampeners
Off-design mixture ratio transient
TURBOPUMP
FAILURE (OR)
Turbopump over-speed / burst
Bearing seizure / rubbing
Cavitation-induced surge
Inducer damage from debris
Seal failure — propellant cross-leak
Pre-burner / gas generator explosion
NOZZLE / CHAMBER
FAILURE (OR)
Nozzle throat burn-through
Nozzle liner burn-through (ablative)
Chamber wall hot spot / burnout
Regenerative cooling blockage
Nozzle extension separation
Manifold crack under pressure
■ = Basic event Nozzle liner burn-through is highlighted as a key accumulated-damage failure mode
Author: Tom Irvine | Vibrationdata

## Slide 7
Branches 3–5 — Structural, Avionics, and Ground Support Failures
Vibrationdata
Supporting branches — individually less likely but potentially correlated with propulsion failures
STRUCTURAL FAILURE (OR)
Airframe overpressure from explosion
Stand hold-down fitting failure
Thrust structure buckling
Thermal protection failure
Explosive bolt misfire
Pre-existing manufacturing crack
LOX-compatible material substitution error
Stage interface ring failure
CONTROL / AVIONICS FAILURE (OR)
Engine controller commands wrong sequence
Abort system fails to safe on anomaly
Sensor gives false-nominal (no abort trigger)
Ignition command sent before ready state
Flight computer software error
EMI corrupts command bus
Redundant channel failure (common cause)
Watchdog timer disabled for test
GSE / HUMAN ERROR (OR)
Propellant loading procedure deviation
Ground valve in wrong position
Umbilical fails to retract at ignition
Purge gas not connected properly
Range safety system bypassed for test
Incorrect hold-down release timing
Maintenance error (wrong component installed)
Communication failure (abort not relayed)
Human factors and GSE errors are often correlated — a single procedural deviation can affect multiple branches simultaneously
Author: Tom Irvine | Vibrationdata

## Slide 8
Branch 6 — Accumulated Fatigue / Prior Test History
Vibrationdata
Each engine has prior hot-fire history from individual acceptance tests — latent damage accumulates before vehicle-level static fire
ACCUMULATED FATIGUE / PRIOR TEST HISTORY (AND/OR)
AND gate: requires (1) prior test history + (2) incomplete inspection + (3) vehicle-level test exceeds remaining margin
TURBOPUMP
DEGRADATION
Bearing wear / spalling from prior high-speed ops
Turbopump seal compression set (elastomeric)
Impeller surface erosion from cavitation cycles
Shaft fatigue from torsional transients at start
Bearing race fretting from vibration during storage
Coolant flow restriction from deposits
COMBUSTION
COMPONENT FATIGUE
Chamber wall low-cycle thermal fatigue (liner)
Nozzle liner ablative material thinning
Injector face cracking from acoustic loading
Pre-burner/gas generator hot-time degradation
Cooling channel blockage (deposit build-up)
Nozzle throat dimensional growth from erosion
PROPELLANT LINE
FATIGUE
Flex bellows fatigue from chill-down thermal cycles
Weld toe cracking from pressure cycling
LOX dome seal set from repeated seating
Check valve spring fatigue
Prevalve seat wear from multiple actuations
Feedline vibration fatigue at support brackets
INSPECTION
GAP (AND gate)
Post-acceptance-test inspection incomplete
Damage below NDT detection threshold
Wrong inspection criteria applied
Inspection not re-performed after shipping
Assembly-induced damage after final inspection
Documentation gap — damage not dispositioned
■ = Basic event The AND gate for inspection gap is critical: adequate post-test inspection breaks this fault path
Author: Tom Irvine | Vibrationdata

## Slide 9
Branch 6 — Cumulative Hot-Time and Inspection Requirements
Vibrationdata
Engine life consumption must be tracked across all tests to quantify remaining margin before vehicle static fire
CUMULATIVE LIFE CONSUMPTION — TYPICAL SCENARIO
Test event
Typical burn
duration
Life fraction
consumed
Cumulative
life used
Individual engine acceptance test #1
8–10 s
10–15%
10–15%
Individual engine acceptance test #2 (if req'd)
8–10 s
10–15%
20–30%
Engine shipping & assembly thermal cycles
—
2–5%
22–35%
Vehicle-level static fire
3–10 s
5–15%
27–50%
First flight burn (stage 1)
150–180 s
30–60%
57–110%
* Life fractions are illustrative; actual values depend on engine design specification and test profile
REQUIRED CONTROLS — FATIGUE BRANCH
Engine life ledger
Track cumulative hot-time, start cycles, chill-down cycles, and pressure cycles per serial number from first acceptance test through flight
Post-test NDT
Borescope combustion chamber, turbopump inspection, dye-penetrant on welds and nozzle weld bands after every hot-fire
Flex line cycle count
Count thermal cycles on each bellows; replace at manufacturer's fatigue limit regardless of visual condition
Seal replacement policy
Replace all elastomeric and metal seals after each hot-fire; do not re-seat previously fired seals
Shipping damage check
Perform full receiving inspection after transport from test facility to launch site; repeat NDT on weld joints
Margin gate
Define minimum remaining life fraction required before vehicle static fire; gate is a no-go if margin is exceeded
Author: Tom Irvine | Vibrationdata

## Slide 10
Common-Cause Failures & Minimum Cut Sets
Vibrationdata
Events that can simultaneously trigger multiple branches represent the highest risk
COMMON-CAUSE FAILURE SCENARIOS
Failure Scenario
Branches Affected
Risk
Ignition sequence software error
Engine + Control
HIGH
LOX leak near ignition source
Propellant + Structural
HIGH
Hard start → turbopump rupture
Engine + Structural
HIGH
Fatigue damage missed at inspection
Fatigue + Engine/Struct
HIGH
Sensor failure masks abort trigger
Control + Human
MED
Ground umbilical not disconnected
GSE + Structural
MED
Wrong purge gas (contaminates propellant)
Propellant + GSE
MED
Pre-existing liner thinning → burn-through
Fatigue + Engine
MED
EMI corrupts command bus
Control + Engine
LOW
MINIMUM CUT SETS (ORDER 1)
Single-point failures sufficient to cause top event:
CS-01
Propellant line rupture near ignition source
CS-02
Engine hard start exceeding chamber design limit
CS-03
Ignition sequence software sends wrong command
CS-04
Relief valve fails closed → tank BLEVE
CS-05
Abort system inhibited + anomaly occurs
CS-06
Turbopump over-speed → burst
CS-07
Ground umbilical not released at ignition
CS-08
LOX leak onto vehicle skin near ignition
CS-09
Nozzle liner burn-through from prior thinning
Author: Tom Irvine | Vibrationdata

## Slide 11
Summary — Fault Tree Results & Preventive Controls
Vibrationdata
Top Event
Vehicle Destruction
at Static Fire
Fault Tree Gates
6 Level-1 OR Branches
25+ Level-2 Sub-events
Highest Risk Path
Propellant Leak +
Ignition Source
PREVENTIVE / MITIGATING CONTROLS BY BRANCH
Propellant System
Leak detection sensors + auto-abort; double-block-and-bleed valves; pre-fire leak check; redundant relief valves
Engine / Combustion
Ignition monitoring before main valve open; chamber pressure abort limits; pre-burner health check; hard-start suppression (water deluge)
Structural
Pre-fire NDT of welds and fittings; stand load cell monitoring; thermal imaging during chill-down; explosive system safing until T-0
Control / Avionics
Independent abort system (hardwired); sensor voting logic (2-of-3); software V&V per NASA-STD-8739.8; all safeties enabled for test
GSE / Human Factors
Two-person integrity for valve line-up; independent verification checklist; automated propellant loading; RSO independent abort authority
Accumulated Fatigue
Engine life ledger per S/N; post-test NDT borescope + dye-penetrant; seal replacement policy; remaining-life gate before static fire
Reference: MIL-STD-882E | NASA SP-2010-580 | AIAA S-122 | NASA-STD-5009 (fatigue & fracture)

## Slide 12
APPENDIX
Case Histories
NASA & SpaceX Static Fire
and Launch Explosions
Selected incidents mapped to fault tree branches — lessons learned and corrective actions

## Slide 13
Appendix A — NASA Case Histories
Vibrationdata
Selected static fire and propulsion explosion events from NASA programs
NASA / North American
January 27, 1967
Structural / GSE
Apollo 1 — Launch Complex 34 Pad Fire
During a plugs-out ground test, a spark ignited the pure oxygen atmosphere in the Command Module. The fire spread rapidly due to flammable materials. All three crew members were lost. Root cause: flammable cabin materials + 100% O₂ atmosphere + inadequate emergency egress.
Lesson: Led to complete cabin redesign, substitution of flammable materials, mixed-gas atmosphere, and overhauled abort and egress procedures.
NASA / Rocketdyne (Saturn V)
April 4, 1968
Engine / Combustion
J-2 Engine Combustion Instability — Apollo 6
Two S-II stage J-2 engines shut down prematurely due to propellant line fatigue failure and combustion instability. Third stage J-2 also failed to restart. Mission continued on reduced profile using remaining engines.
Lesson: Resulted in redesign of the LOX prevalve and feedline, and improved injector baffling to suppress high-frequency combustion instability.
NASA / MSFC
November 1, 1999
Structural / Propellant
X-33 Liquid Hydrogen Tank Failure
The composite LH₂ tank on the X-33 technology demonstrator failed during a ground test at Stennis Space Center. Internal delamination allowed LH₂ to penetrate the composite overwrap; the tank burst. No casualties.
Lesson: Highlighted LH₂ permeation risk in composite tanks; led to revised composite cryogenic tank design criteria and inspection requirements.
NASA / Aerojet
2008–2010 (multiple)
Engine / Combustion
Ares I-X / J-2X Development Engine Test Anomalies
During J-2X engine development tests at SSC, multiple hard-start and ignition sequencing anomalies occurred, including transient chamber pressure spikes approaching design margins. No vehicle loss but test stand damage in two incidents.
Lesson: Reinforced use of spark torch igniter health monitoring and forced addition of igniter-confirm interlocks before main propellant valve opening.
Author: Tom Irvine | Vibrationdata

## Slide 14
Appendix B — SpaceX Case Histories
Vibrationdata
Selected static fire and launch pad explosion events from SpaceX Falcon 9 and Starship programs
SpaceX
June 28, 2015
Structural / Propellant
CRS-7 / Falcon 9 — In-Flight Breakup
Falcon 9 broke up approximately 139 seconds after launch while carrying Dragon CRS-7. A strut in the second-stage LOX tank failed well below its rated load, causing the tank to over-pressurize and rupture. The vehicle was destroyed; no crew aboard.
Lesson: Supplier quality control procedures were substantially revised; strut design loads re-verified by independent test; acceptance test criteria tightened for all structural fasteners and supports.
SpaceX
September 1, 2016
Propellant System
AMOS-6 / Falcon 9 — Static Fire Pad Explosion
During routine pre-launch static fire propellant loading, a COPV in the second-stage LOX tank failed. Supercooled liquid oxygen trapped in the carbon fiber overwrap ignited when compressed by helium loading. Vehicle and payload destroyed on the pad at LC-40.
Lesson: COPV design was modified to eliminate the oxygen entrapment failure mode; loading procedures and temperature monitoring revised; new COPV qualification approach adopted.
SpaceX
April 20, 2023
Engine / Control / GSE
Starship IFT-1 — Rapid Unscheduled Disassembly
During first integrated flight test, multiple Raptor engines failed at liftoff, the vehicle began to roll uncontrollably, and FTS activated at T+~4 min. Pad infrastructure was severely damaged by exhaust, which excavated the foundation due to absence of a water deluge system.
Lesson: Flame deflector / water deluge system added for IFT-2 onward; engine-out performance margins reassessed; FTS activation thresholds reviewed; Mechazilla catch system accelerated.
SpaceX
November 18, 2023
Control / Avionics
Starship IFT-2 — Vehicle Loss at Stage Separation
Super Heavy booster executed hot-stage separation and its FTS activated over the Gulf of Mexico. Starship upper stage reached ~148 km before FTS was commanded following a propellant leak and loss of attitude control during the RCS burn. Both vehicles intentionally destroyed.
Lesson: Propellant system leak isolation procedures improved; redundant FTS command paths verified; attitude control authority margins for RCS increased prior to IFT-3.
Author: Tom Irvine | Vibrationdata

## Slide 15
Appendix C — Case History Cross-Reference to Fault Tree Branches
Vibrationdata
Each historical event maps to one or more Level-1 fault tree branches — fatigue branch added
Event
Date
Propellant
System
Engine /
Combust.
Structural
Control /
Avionics
GSE /
Human
Accum.
Fatigue
Primary Cause
Apollo 1 Pad Fire
1967
Flammable O₂ atmosphere
Apollo 6 J-2 Instability
1968
Combustion instability + fatigue
X-33 LH₂ Tank
1999
Composite tank delamination
J-2X Test Anomalies
2008–10
Hard-start / ignition sequencing
Falcon 9 CRS-7
2015
Structural strut failure
Falcon 9 AMOS-6
2016
COPV oxygen entrapment
Starship IFT-1
2023
Multi-engine failure + pad damage
Starship IFT-2
2023
Propellant leak + attitude ctrl loss
● = Primary contributing branch (purple = accumulated fatigue) Sources: NASA LLIS, SpaceX FAA mishap reports, AIAA conference papers