## Slide 1
VIBRATIONDATA TECHNICAL BRIEFING
Spacecraft On-Orbit Vibration
Microvibration & Jitter: Design • Analysis • Testing • Mitigation
Reaction Wheels
Cryocoolers
Mechanisms
Structural Path
Source: Tom Irvine, “Spacecraft On-orbit Vibration,” Vibrationdata Blog, June 12, 2014 (blog.vibrationdata.com)
Vibrationdata

## Slide 2
Vibrationdata
Briefing Roadmap
Four parts: the full jitter problem from root cause to flight mitigation
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
2
1
Foundations
What jitter is, how it degrades optical performance, and the source taxonomy
2
Design
Architectural strategies: isolation, structural stiffness, mechanism choice
3
Analysis
Disturbance modeling, transfer paths, and line-of-sight error budgets
4
Testing & Mitigation
Ground verification challenges and flight-proven suppression methods

## Slide 3
Acronyms and Abbreviations
Vibrationdata
Key terms used throughout this briefing
ACS
Attitude Control System
ASD
Acceleration Spectral Density
CB
Craig-Bampton (substructuring)
CBE
Current Best Estimate
CMG
Control Momentum Gyro
CSD
Cross-Spectral Density
DOF
Degree of Freedom
ECSS
European Cooperation for Space Standardization
FE / FEM
Finite Element / Finite Element Model
FRF
Frequency Response Function
FSM
Fast Steering Mirror
GNC
Guidance, Navigation & Control
HST
Hubble Space Telescope
IFOV
Instantaneous Field of View
IR
Infrared
JWST
James Webb Space Telescope
LFT
Linear Fractional Transformation
LOS
Line of Sight
LSS
Large Space Structure
MLI
Multi-Layer Insulation
MTF
Modulation Transfer Function
MVIS
Miniature Vibration Isolation System
NICMOS
Near-Infrared Camera / Multi-Object Spectrometer
NTRS
NASA Technical Reports Server
PSD
Power Spectral Density
RF
Radio Frequency
RMS
Root Mean Square
RSS
Root Sum Square
RWA
Reaction Wheel Assembly
SADM
Solar Array Drive Mechanism
SDM
Structural Dynamics Model
STOP
Structural-Thermal-Optical Performance
TPA
Transfer Path Analysis
TVac
Thermal Vacuum (test)
VISS
Vibration Isolation & Suppression System
WFE
Wavefront Error
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
3

## Slide 4
PART 1
Foundations
Defining microvibration / jitter and why it is a whole-spacecraft problem
4

## Slide 5
Vibrationdata
What Is Spacecraft Jitter?
Low-level, self-induced vibration generated by the spacecraft's own moving parts on orbit
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
5
Definition
Vibration the spacecraft generates internally once it reaches orbit and becomes operational — distinct from pre-launch transport or powered-flight loads
Predominantly sinusoidal with integer harmonics (from rotating machinery); broadband random content from bearing noise and cryocooler compressors is also present
Amplitudes are typically in the micro-g range (10−6 to 10−3 g), yet they couple directly into sensitive payload performance because optical instruments have nano-radian pointing requirements
ECSS-E-HB-32-26A frames the working microvibration band as roughly 1 Hz up to 500–1000 Hz — below ~1 Hz the ACS can compensate; above ~1 kHz structural attenuation is sufficient
Why It Matters
Degrades line-of-sight pointing for optical instruments, laser communication terminals, and interferometric baselines
Smears imagery and broadens the point-spread function on Earth-observation and astronomical platforms during integration time
Couples into structural resonances, amplifying otherwise small disturbance forces by an order of magnitude or more
Unlike launch loads, jitter is continuous and operationally persistent — it must be managed for mission life, not survived once

## Slide 6
Vibrationdata
A System-Level Problem
Jitter must be solved across the full source → structure → sensor chain
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
6
Disturbance
Source
Structural
Transfer Path
Isolation /
Damping
Sensitive
Payload
Wheel, cryocooler,
mechanism
Bus, booms,
mounting structure
Passive or active
attenuation
Optics, sensors,
pointing system
Takeaway: Effective jitter control requires coordinated attention at every link in this chain — not a single fix at the source.

## Slide 7
Vibrationdata
Four System-Level Suppression Strategies
How jitter can be addressed at the spacecraft system level
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
7
Reduce Payload Sensitivity
Design the payload to tolerate microvibration, or mechanically isolate it from the rest of the spacecraft bus
Reduce Transmissibility
Design the spacecraft structure itself to attenuate disturbance transmission from source to payload
Post-Process Imagery
Mitigate residual jitter effects after the fact through image processing and reconstruction
Reduce Source Noise
Manage microvibration by lowering the mechanical noise generated at the source, or isolating the noise source itself

## Slide 8
Vibrationdata
Effects of Jitter on Optical Instruments
How line-of-sight motion at the focal plane degrades imaging, pointing, and laser performance
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
8
Imaging Degradation
Line-of-sight motion during an exposure smears the point-spread function, reducing modulation transfer function (MTF) at high spatial frequency
Jitter components faster than the detector integration time blur the image; components slower than integration time appear as frame-to-frame pointing error instead
Push-broom and scanning imagers are especially sensitive because cross-track jitter directly mis-registers successive image lines
For diffraction-limited optics, jitter approaching a fraction of the diffraction-limited spot size can dominate the total error budget over optical aberrations
Pointing & Coherent-Optics Effects
Fine star trackers and guide-camera loops can be driven by the same structural jitter they are trying to measure, coupling sensor noise back into the control loop
Free-space laser communication terminals lose link margin rapidly as pointing jitter approaches the transmit beam divergence angle
Long-baseline or segmented-mirror telescopes accumulate differential jitter between segments as wavefront error, not just simple image blur
Interferometric and coronagraphic instruments are sensitive to jitter-induced optical path-length changes of a small fraction of a wavelength

## Slide 9
Vibrationdata
Quantifying the Impact: Modulation Transfer Function vs. Jitter Amplitude
Even sub-pixel line-of-sight jitter measurably reduces contrast at high spatial frequency
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
9
Reading the Curve
Curves show the MTF attenuation factor contributed by random (Gaussian) jitter alone, for several jitter standard deviations expressed as a fraction of one detector pixel / IFOV
Attenuation is negligible at low spatial frequency but grows sharply approaching Nyquist — fine image detail is lost first
A jitter σ of just 0.1–0.2 pixel can already cut high-frequency MTF by 20–40%, which is why fine-pointing requirements are often stated in milli-pixels or microradians
This MTF loss multiplies with the optical system's own diffraction- and aberration-limited MTF — jitter is rarely the only contributor, but it is often the most controllable one

## Slide 10
Vibrationdata
Microvibration Source Taxonomy
Per ECSS-E-HB-32-26A: harmonic and transient disturbance sources on a typical spacecraft
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
10
Harmonic / Rotating Sources
Reaction wheels
Control momentum gyros
Gyroscopes
Solar array drive mechanisms
Antenna pointing mechanisms
Mirror scan mechanisms
Cryogenic coolers
Transient / Non-Moving Sources
Micro-thrusters, gas flow regulators
Latch valves
Heat pipes
Relays, RF switches
Sudden stress release (“thermal snap”)
Clank phenomena (e.g., MLI foil buckling)

## Slide 11
Vibrationdata
Microvibration Source Frequency Map
Where each disturbance lands on the frequency axis — and where the payload is most vulnerable
Reading the Map
Each rotating source paints a fan of lines: forcing frequency = wheel speed × harmonic index, so the disturbance sweeps as the wheel changes speed
Payload-sensitive structural modes are horizontal bands — trouble occurs where a harmonic line crosses a mode
Cryocooler tones sit at fixed frequencies (20–60 Hz Stirling); Brayton turbines live far above the band at 3–13 kHz
The crossing points define the wheel speeds to avoid — the “no-spin zones” quantified later in the Analysis section
Takeaway: Plotting every source on one speed–frequency map turns jitter risk into a geometry problem: keep the harmonic lines off the structural modes.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
11

## Slide 12
Vibrationdata
Reaction Wheels: Operating Principle
The dominant attitude-control disturbance source on most spacecraft
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
12
Flight reaction / momentum wheel assembly
Flywheels driven by electric motors, commanded by the attitude control computer
Typically, three wheels mounted on mutually perpendicular axes, with a fourth skewed wheel often added for redundancy
Operate per Newton's Third Law and conservation of angular momentum: changing wheel speed exerts a reaction torque on the spacecraft
The acceleration ratio between wheel and spacecraft equals the inverse ratio of their moments of inertia
Especially valuable for very fine pointing — keeping a telescope trained on a star or holding an antenna or laser steady
A representative commercial momentum wheel spans a speed range of ±10,000 rpm (167 Hz); the Kepler telescope's wheels operated between 1000 and 4000 rpm in both directions
Takeaway: Because the wheel is the actuator for fine attitude control, its disturbance signature cannot simply be eliminated — it must be managed.

## Slide 13
Vibrationdata
Reaction Wheel Disturbance Spectrum
Motor noise, imbalance, and bearing disturbances produce a fundamental plus integer harmonics
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
13
Key Mechanisms
Electrical motor noise (commutation, cogging torque)
Static and dynamic mass imbalance at wheel speed
Bearing-induced disturbances and ball-pass frequencies
Forcing occurs at wheel speed and its integer harmonics
Imbalance harmonics can excite structural resonances during angular acceleration through a critical speed

## Slide 14
Vibrationdata
Wheel Saturation and Desaturation
Momentum management introduces its own transient disturbance events
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
14
1
Momentum Builds
External torques (solar pressure, gravity gradient, magnetic) steadily load the wheels
2
Saturation
Wheel speed approaches its operational limit and can no longer absorb further momentum
3
Desaturation Burn
Thrusters fire to offload momentum while wheels are commanded toward rest
4
Cycle Repeats
As unbalanced torque rebuilds, wheels spin back up toward saturation
Alternative momentum management: magnetorquers (electromagnetic coils) can offload momentum against the Earth's magnetic field without firing thrusters, avoiding the transient plume disturbance and propellant cost of a desaturation burn — though they are limited by orbit altitude and field strength.

## Slide 15
Vibrationdata
Cryocoolers: Overview
Miniature refrigerators that enable cryogenic detector technologies
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
15
Cool sensitive spacecraft components to cryogenic temperatures for infrared, gamma-ray, and x-ray detectors
The largest current usage is in Earth Science instruments operating near the boiling point of liquid nitrogen, 77 K (−321°F)
Working fluid is typically hydrogen or helium, cycled from gaseous to liquid form and boiled back to gas
Compressors with rotating and/or reciprocating parts generate vibration as they cycle gas through phase changes
Vibration is typically mitigated with active control — commonly an electromechanical counterbalance mass or a piezoelectric driver
Example Application
JWST MIRI Instrument Cryocooler
Cold head (top) and compressor/precooler assembly (bottom) used to cool the Mid-Infrared Instrument detectors to operating temperature

## Slide 16
Vibrationdata
Cryocooler Types and Drive Frequencies
Three common cooler architectures span vastly different operating frequency bands
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
16
Type | Mechanism | Frequency Range
Joule-Thomson (J-T) Sorption | Solid-state compressor; isenthalpic expansion across a valve | < 1 cycle/hour
Oxford-Style Stirling | One or two pistons; most common cryocooler type | 1200–3600 rpm (20–60 Hz)
Reverse Turbo-Brayton | Tiny high-speed turbines | 200,000–800,000 rpm (3.3–13 kHz)

## Slide 17
Vibrationdata
Stepper Motors
Brushless DC motors that divide rotation into discrete commandable steps
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
17
Typical Applications
Driving solar arrays
Pointing antennas
Mobile mirror drives
Hold-down and release mechanisms
Disturbance Mechanism
Position is commanded open-loop to a discrete step, without feedback sensing, as long as the motor is properly sized to the load
The motor itself, plus any accompanying gear meshing, generates transient vibration as force and torque disturbances
Transmitted force can degrade the quality of optical images recorded by a camera elsewhere on the spacecraft
4-phase stepper: stator coils energized in sequence step the multi-toothed magnetic rotor — each transition is a small, discrete torque impulse

## Slide 18
Vibrationdata
Non-Moving Disturbance Sources
Vibration can arise even without continuously rotating or reciprocating hardware
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
18
Electronics & Sensors
Switching transients and relay/RF-switch actuation generate brief mechanical impulses
Thermal Snap
Sudden release of stored strain energy at structural interfaces — joints, latches, hinges — as thermal loads shift
Thermally-Induced Bending
Solar arrays, antennas, and other deployables flex as they cross the orbital terminator and experience sudden temperature change
Clank Phenomena
Electromagnetic force effects and buckling of multi-layer insulation (MLI) foil produce impulsive transients

## Slide 19
PART 2
Design
Architectural choices that prevent jitter problems before they reach hardware
19

## Slide 20
Vibrationdata
Design Decision Logic: Choosing the Intervention
A single flow that ties source selection, isolation, and structural design together
Is the disturbance above the ACS control bandwidth (>1 Hz)?
NO — ≤ 1 Hz
YES — > 1 Hz
Let the ACS Absorb It
Slow drifts and bias are corrected by the attitude-control loop
No mechanical mitigation needed in this band
Verify the loop has authority and bandwidth margin
Quiet the Source
Higher wheel-balance grade; active cooler balancers
Closed-loop stepper control; slower slew profiles
Cheapest fix when feasible — less energy to manage downstream
Isolate & Detune the Path
Soft-mount the payload or the source (passive / active)
Separate source and payload structural modes (≥2×)
Add damping at high modal-strain-energy nodes
Reserve sway space for the isolator stroke
Takeaway: Most jitter problems are solved by a combination of all three branches — the flow shows which lever to reach for first, not the only lever to pull.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
20

## Slide 21
Vibrationdata
Design Philosophy: Where to Intervene
Jitter mitigation is most effective — and least costly — the earlier it is designed in
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
21
Concept
Select mechanisms and source hardware with inherently lower disturbance signatures
Architecture
Locate sensitive payloads away from disturbance sources; plan structural load paths
Detailed Design
Size isolators, dampers, and stiffness to meet allocated transmissibility budgets
Verification
Confirm performance by test and analysis before committing to flight hardware
Takeaway: Cost of fixing a jitter problem grows roughly an order of magnitude at each stage moved to the right — design decisions made early carry the most leverage.

## Slide 22
Vibrationdata
Design Strategy: Payload Isolation
Mechanically decouple the sensitive payload from the disturbance-generating bus
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
22
Mount the sensitive instrument on a dedicated isolation platform rather than rigidly to the spacecraft structure
Passive isolators (elastomeric, wire-rope, or spring-and-damper) attenuate disturbance above their corner frequency
Isolator corner frequency must sit well below the lowest critical disturbance frequency — typically the reaction wheel speed range
Lowering the corner frequency to gain jitter attenuation increases the relative displacement the isolator must accommodate across its full operating envelope, not just at resonance
Soft isolation can conflict with launch-load stiffness requirements; many designs use launch locks, motion-limiting snubbers, or stroke stops to bound relative displacement during ascent
Multi-axis isolation (6-DOF platforms) addresses coupled translational and rotational disturbance paths simultaneously, but must budget relative displacement in every axis independently
Relative Displacement Trade
Softer isolation
= better jitter attenuation
but larger relative
displacement (sway space)
and slower settling after
maneuvers or slews.
Stiffer mounting
= faster settling
but higher disturbance
transmission to payload.

## Slide 23
Vibrationdata
Relative Displacement and Isolator Selection
Closing the corner-frequency trade with a real device that survives vacuum and on-orbit temperature swings
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
23
Design rule: size the isolator's working stroke (or the structure's keep-out / sway-space envelope) to the predicted relative displacement at the softest corner frequency under consideration, with margin for fabrication and thermal offset — not just the on-orbit micro-g amplitude.
Isolators Suited to Vacuum / Thermal Extremes
D-strut / viscous three-parameter strut
Honeywell-heritage strut combining a soft spring in parallel with a viscous-fluid damper; flight-proven on HST (reaction wheel isolation), VISS, and MVIS. Damping fluid must be selected for stable viscosity from cryogenic to elevated temperature, and bellows-sealed against vacuum exposure.
Wire-rope isolator
All-metal stranded-cable element; damping is Coulomb friction between strands. No elastomer to outgas or embrittle, making it tolerant of wide temperature swings and hard vacuum, though stiffness and damping vary somewhat with input amplitude and require test-based characterization.
Viscoelastic-damped strut (constrained-layer) Titanium or graphite-epoxy flexures with a constrained viscoelastic damping layer, as used on JWST's instrument isolators. Requires a low-outgassing, radiation-tolerant viscoelastic formulation whose loss factor is characterized over the full flight temperature range, since elastomer damping is intrinsically temperature- and frequency-dependent.
.

## Slide 24
Vibrationdata
Design Strategy: Structural Transmissibility
Shape the spacecraft structure itself to attenuate the path from source to sensor
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
24
Separate disturbance-source mounting frequencies from payload-sensitive frequencies — avoid coincident structural modes along the transfer path; a frequency separation ratio of at least 2× is a common rule of thumb
Increase local stiffness and mass at the source mount to reduce coupled motion into the bus structure; a stiff, well-isolated source mount can reduce transmitted force by 10–20 dB without a dedicated isolator
Add structural damping (viscoelastic constrained layers, tuned mass dampers) at node locations identified by transfer-path analysis, where modal strain energy density is highest
Route load paths so that disturbance energy is directed away from, rather than through, sensitive instrument mounts — orthogonal load paths between RWAs and optical bench are particularly effective
Avoid placing reaction wheels, cryocoolers, or other rotating machinery on panels that share a structural mode with the payload bench — stiffened close-out ribs can detune a shared panel mode by 30–60%
Maintain mass budget discipline: added stiffening mass is only effective if it shifts the mode, not just the mode shape — target modifications where modal effective mass is highest
Takeaway: Modal separation between source and payload mounting structure is often the single most cost-effective structural design lever for jitter.

## Slide 25
Vibrationdata
Design Strategy: Source Selection
Choosing inherently quieter hardware reduces the disturbance the rest of the system must absorb
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
25
Design Lever | Application
Higher wheel-balance grade | Reaction / momentum wheels — tighter static and dynamic balance specs reduce imbalance harmonics
Active cooler balancers | Cryocoolers — electromechanical counterbalance mass or piezo driver cancels compressor-induced force
Magnetorquer-first momentum control | Reduces frequency of thruster desaturation burns and their transient disturbance
Closed-loop stepper control | Stepper-driven mechanisms — feedback sensing allows smoother, lower-impulse motion profiles
Slower mechanism slew profiles | Antenna / mirror pointing drives — trades settling time for reduced peak transient force

## Slide 26
Vibrationdata
Active & Hybrid Jitter Control
When passive isolation is not enough: adding sensors, actuators, and a control loop
Why Go Active
Passive isolators cannot attenuate below their corner frequency and amplify at resonance — active control fills exactly that gap
Active systems add low-frequency disturbance rejection and can null specific tonal lines that a passive mount passes through
Penalty: actuators, sensors, power, control electronics, and the risk of closed-loop instability
Used when the LOS budget cannot be met passively — high-resolution imaging and laser-comm terminals are the usual drivers
Active Techniques
Fast steering mirror (FSM): a small actuated mirror closes the residual line-of-sight loop downstream of the structure
Active isolation platform: voice-coil or piezo actuators on a Stewart (hexapod) frame cancel motion in 6 DOF
Feed-forward cancellation: a wheel-speed tachometer signal predicts the harmonic and drives an anti-phase force
Active counterbalancer: piezo / electromagnetic mass cancels the cryocooler compressor force at its source
Takeaway: Active control buys low-frequency and tonal rejection that passive mounts physically cannot — at the cost of power, complexity, and a stability budget.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
26

## Slide 27
Vibrationdata
Active–Passive Crossover Strategy
Pair each method where it works best: active below the corner, passive above
Reading the Curve
Below the isolator corner the passive mount does nothing and amplifies at resonance — the active loop suppresses that peak
Above the corner the passive roll-off (~40 dB/decade) already does the work, so the active loop hands off
The hybrid curve keeps the passive high-frequency attenuation while removing the resonant amplification
Crossover frequency is a design choice: push it higher for more active authority, lower to save actuator effort and power
Takeaway: The best architectures are hybrid — active control owns the resonance and the sub-corner band; the passive mount owns the high-frequency roll-off.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
27

## Slide 28
Vibrationdata
Design Section Summary
Four complementary design levers, applied together rather than in isolation
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
28
Isolate the Payload
Soft-mount sensitive instruments; manage the launch-lock trade
Separate the Modes
Keep source and payload structural frequencies apart
Pick Quieter Hardware
Specify balance grades, active balancers, closed-loop control
Manage Momentum Smartly
Favor magnetorquers to reduce desaturation transient frequency

## Slide 29
PART 3
Analysis
Predicting jitter response before hardware is built or tested
29

## Slide 30
Vibrationdata
Disturbance Modeling Approach
Representing source forces so they can be propagated through a structural model
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
30
Source Characterization by Type
Reaction wheels: empirical harmonic coefficient tables (Ci) measured on a dynamometer — amplitude of each harmonic = Ci × Ω², where Ω is wheel speed in rad/s
Cryocoolers: fixed-frequency line spectra plus broadband noise floor; noise floor modeled empirically as speed-dependent polynomial (Blaurock 2009)
Stepper motors and latch/valve events: transient force-torque time histories captured by multi-axis load cell at the mount interface
Thermal snap / clank: statistical impulsive loads bounded from heritage data or finite-element contact analysis
Multi-Source Coherence Treatment
Multiple disturbance sources (three RWAs, one cryocooler) act simultaneously — they are rarely coherent at a single frequency, so root-sum-square (RSS) combination is the default
If sources share a structural path or drive frequency, partial coherence can increase response by up to 6 dB above RSS — cross-spectral density treatment is then required
Broadband noise contributions are combined in power (PSD addition), while deterministic harmonics are combined as phasors if coherence data exists, or as upper-bound RSS otherwise
Disturbance models must be validated against spin-table or TVac force-measurement data before insertion into the system model — an unvalidated model can be optimistic by 2–5×
Takeaway: The fidelity of the jitter prediction can never exceed the fidelity of the underlying disturbance model — garbage in, garbage out.

## Slide 31
Vibrationdata
Force-to-Jitter Transfer Path Analysis
Standard FE methods apply — but with several adaptations specific to the micro-g amplitude regime
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
31
Workflow
Build a structural FE model spanning source mount to sensitive payload mount; include isolators, flexible appendages, and any non-structural mass that participates in the transfer path
Apply disturbance force/torque model at the source interface node(s) and compute frequency response functions (FRFs) via modal superposition
For harmonic sources (RWA): evaluate FRF at each harmonic frequency as wheel speed sweeps — resonance crossings produce transient peak responses that may exceed steady-state predictions
For broadband/random sources (noise floor): convolve disturbance PSD with |H(f)|² (output PSD = disturbance PSD × FRF squared), then integrate to RMS
Propagate nodal response to optical LOS using the instrument optical sensitivity matrix
Compare RSS of all contributors against the allocated jitter requirement with appropriate margin
Jitter-Specific FE Adaptations
On-orbit boundary conditions: the spacecraft floats free — the model must use free-free or inertia-relief boundary conditions, not a fixed base as in launch-load analysis
Micro-g amplitude regime: elastomeric isolator stiffness is amplitude-dependent; at micro-g excitation levels it may be 3–10× stiffer than its 1g static value, requiring amplitude-corrected material properties
Modal density: jitter analysis typically extends to 500–1000 Hz, requiring a denser mode set and higher mesh resolution than standard mode-survey correlation models
Damping uncertainty: structural damping at micro-g amplitudes is poorly characterized; sensitivity studies spanning at least 0.3–3× nominal damping are standard practice
Craig-Bampton + residual vectors: necessary to accurately capture quasi-static response from high-frequency disturbances applied above the modal cutoff of each substructure
Takeaway: Standard FE machinery is reused, but jitter analysis adds jitter-specific inputs, on-orbit boundary conditions, and a micro-g amplitude regime that standard launch-load practice does not address.

## Slide 32
Vibrationdata
STOP Analysis: The Jitter-Specific Model Chain
Integrated Structural–Thermal–Optical Performance analysis links FE, thermal, and ray-trace models
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
32
Disturbance
Model
Empirical harmonic tables + broadband noise floor from component test
Structural
FE Model
On-orbit free-free BC; CB/Guyan reduction; micro-g amplitude-corrected isolator stiffness
Optical
Sensitivity
Matrix
Jacobian from structural DOFs to LOS/WFE; derived from ray-trace model (Zemax, Code V)
LOS / WFE
Prediction
RSS of harmonic + random + thermal contributors; compared to allocated jitter budget
What makes STOP jitter-specific: the optical sensitivity matrix and its derivation from the ray-trace model is unique to jitter work — it does not appear in standard launch-load or modal analysis.

## Slide 33
Vibrationdata
Harmonic Sweep vs. PSD Random Analysis
Choosing the right computational approach for each disturbance class
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
33
Harmonic Sweep Analysis
Used when the disturbance is deterministic and tonal: RWA imbalance harmonics, cryocooler piston frequency and its integer multiples
Sweep wheel speed across the operational range; evaluate FRF at each harmonic frequency f = i×Ω/2π (i = harmonic index, Ω = spin rate in rad/s)
Resonance crossings produce amplified peak responses that must be bounded; peak depends on sweep rate, damping, and structural modal density
Output: peak and RMS LOS amplitude as a function of wheel speed; used to identify “no-spin-zone” speed exclusion bands
Limitation: cannot capture broadband noise or stochastic disturbances; deterministic phase is unknown, so amplitudes are combined as RSS across harmonics
PSD / Random Vibration Analysis
Used for broadband noise floor (RWA bearing noise, cryocooler broadband), jitter from acoustic environments, and thermally induced random disturbances
Response PSD at the optical bench: Sₓₓ(f) = |H(f)|² × Sᶠᶠ(f), where H(f) is the structural FRF and Sᶠᶠ is the disturbance input PSD
RMS jitter = √∫ Sₓₓ(f) df integrated over the relevant frequency band; dominant contribution usually near structural resonances
Multi-input systems require a cross-spectral density matrix: S_out = H × S_in × Hᴴ, where H is the matrix of FRFs between all inputs and the output
Limitation: requires well-characterized broadband disturbance PSDs; these are harder to measure at micro-g levels than harmonic amplitudes
Takeaway: In practice both methods are run together: harmonic sweep for tonal RWA lines, PSD analysis for the noise floor — the combined RSS gives total predicted jitter.

## Slide 34
Vibrationdata
Passive Isolator Transmissibility Analysis
Damping ratio governs both resonant amplification and high-frequency roll-off
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
34
Reading the Curve
Below resonance: transmissibility ≈ 1, isolator has little effect
Near resonance (f = fₙ): amplification peaks; low damping ζ produces the largest, sharpest peak
Above resonance: transmissibility rolls off near 40 dB/decade for light damping
Heavier damping reduces the resonant peak but also degrades high-frequency attenuation

## Slide 35
Vibrationdata
Line-of-Sight (LOS) Error Budget
Translating predicted micro-g structural motion into pointing or image-quality performance
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
35
Optical Sensitivity Matrix
A Jacobian A relating structural DOFs at the optical bench to LOS error or wavefront error: δLOS = A × δq, where δq is the vector of nodal displacements/rotations
Derived from the ray-trace model (Zemax, Code V) by perturbing each optical element DOF individually and computing the resulting image-plane shift or WFE change
Typically a sparse matrix: only elements of the primary mirror, secondary mirror, focal-plane assembly, and any intermediate optics carry significant sensitivity coefficients
Sensitivity to rigid-body tilt of the primary mirror is usually the dominant term; translation and higher-order deformation terms are smaller by a factor of f/#
Matrix must be revalidated whenever the optical prescription changes — it is not a one-time deliverable
Budget Structure and Typical Values
Total LOS allocation apportioned across: RWA harmonic jitter, RWA broadband noise, cryocooler tonal + broadband, thermal snap transients, control-system tracking error, and unallocated margin
Contributors are combined as RSS under an incoherence assumption; if any two contributors share a structural resonance, coherent addition may apply and RSS is non-conservative
Representative fine-pointing missions: Hubble ≈0.007 arcsec RMS; JWST line-of-sight stability ∼1–2 milli-arcsec (7–14 nrad) RMS over imaging timescales
Budget margin (typically 10–20%) is reserved for un-modeled sources discovered during integration and test — consuming margin early in design is a common program risk
Budget is a living document: updated at each design milestone as disturbance models are refined and test data replaces analysis predictions
Takeaway: An LOS budget is only as credible as its weakest input — every contributor needs either test-correlated data or a conservatively justified bound.

## Slide 36
Vibrationdata
Wheel-Speed Scheduling: No-Spin Zones
Turning a resonance-crossing analysis into an operational speed-exclusion table
How It Works
Sweep predicted LOS jitter across the full wheel-speed range from the harmonic-sweep analysis
Wherever a harmonic crossing pushes jitter above the LOS allocation, that speed band is prohibited
Flight software commands wheels to skip the excluded bands — dwelling only at quiet speeds
Trade: fewer available speeds can reduce momentum-management flexibility, so zones are kept as narrow as the analysis allows
Takeaway: A no-spin zone converts a structural resonance problem into a simple operational constraint — the wheel is commanded never to dwell where the crossing lives.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
36

## Slide 37
Vibrationdata
Analysis Validity Checks
Confidence-building steps before trusting a jitter prediction
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
37
Model Correlation
Compare predicted modal frequencies and shapes against modal survey test data before using the model for jitter prediction
Mesh & Reduction Convergence
Confirm that Craig-Bampton or Guyan reduction order does not distort the frequency range of interest
Disturbance Model Pedigree
Trace every force input back to a component-level test or a documented, justified analytical source
Sensitivity Study
Vary uncertain parameters (damping, mass properties, mounting stiffness) to bound the predicted response

## Slide 38
PART 4
Testing & Mitigation
Ground verification challenges and flight-proven suppression techniques
38

## Slide 39
Vibrationdata
Ground Microvibration Test Methods
Characterizing disturbance sources and verifying jitter performance before launch
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
39
Component-Level Tests
Reaction wheel spin-table testing on a dynamometer or force table across the full operational speed range
Cryocooler vibration characterization on a quiet isolated bench, often inside a thermal/vacuum chamber
Stepper-motor and mechanism transient force measurement using a multi-axis force/torque sensor at the mount interface
System-Level Tests
Integrated spacecraft jitter test with flight-representative disturbance sources operating and a calibrated optical or laser pointing reference
Modal survey test to correlate the structural FE model used for transfer-path predictions
End-to-end LOS stability test with the actual sensor/instrument recording its own pointing performance

## Slide 40
Vibrationdata
Verification Challenges: 1g vs. 0g
Ground test conditions never perfectly replicate the on-orbit environment
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
40
Gravity preloads bearings, isolators, and deployable structures differently than the unloaded, free-floating orbital condition
Suspension or air-bearing fixtures used to approximate free-free boundary conditions introduce their own low-frequency dynamics that must be isolated from the data
Ambient ground vibration and acoustic noise floors can mask the very low-amplitude (micro-g) signals of interest, requiring a quiet test facility or careful noise-floor characterization
Thermal/vacuum testing is often necessary because cryocooler and mechanism disturbance signatures change with operating temperature
Test-to-flight correlation typically relies on the structural model: ground test data validates the model, and the validated model is then used to predict the 0g flight condition
Takeaway: Because jitter cannot be fully verified by ground test alone, the analytical model — correlated to test — carries the final burden of flight prediction.

## Slide 41
Vibrationdata
Flight-Proven Mitigation Techniques
Passive and active methods used to suppress jitter once a source is identified
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
41
Passive Isolation
Elastomeric or wire-rope mounts at the source or payload interface attenuate above the isolator corner frequency with no power or control needed
Active Counterbalancing
Electromechanical or piezo-driven counter-mass cancels cryocooler compressor force at its source, used widely on JWST-class cryocoolers
Magnetorquer Desaturation
Replaces or supplements thruster desaturation burns, removing a transient disturbance event from the timeline entirely
Image Post-Processing
Residual jitter recorded by onboard gyros or star trackers is used to deconvolve or co-register smeared imagery on the ground

## Slide 42
Vibrationdata
Measuring Micro-g: Test Instrumentation
The sensing and facility problem behind every ground microvibration test
Sensors & References
Low-noise seismic accelerometers (force-balance / capacitive) reach the sub-micro-g noise floor that piezo units cannot
Multi-axis force / reaction tables capture the full six-component disturbance at a source mount
Laser interferometers and autocollimators provide a direct optical line-of-sight reference, independent of the structure
Star-tracker or rate-gyro data gives the on-board pointing reference reused later for image post-processing
The Facility Noise Floor
Building HVAC, foot traffic, and ground motion can exceed the micro-g signal of interest by orders of magnitude
Tests run on a seismically isolated slab or pneumatic optical table, often at night, to lower the ambient floor
The measurement noise floor must be characterized and shown to sit below the disturbance being verified
Thermal-vacuum chambers add their own pumps and cold-head vibration — a disturbance source inside the test itself
Takeaway: You cannot verify a disturbance you cannot measure — micro-g testing is as much a quiet-facility and noise-floor problem as a sensor problem.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
42

## Slide 43
Vibrationdata
References and Further Reading
Key documents, handbooks, and peer-reviewed references for spacecraft jitter engineering
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
43
NASA Documents
Dennehy, C. & Alvarez-Salazar, O.S. (2018). “Spacecraft Micro-Vibration: A Survey of Problems, Experiences, Potential Solutions, and Some Lessons Learned.” NASA/TM-2018-220075, Langley Research Center. ntrs.nasa.gov/citations/20180006315
Dennehy, C., Wolf, A.A., & Swanson, D.K. (2021). “Spacecraft Line-of-Sight Jitter Management and Mitigation.” NASA/TM-20210017871. ntrs.nasa.gov/citations/20210017871
NASA NESC Technical Assessment (2025). “Spacecraft Jitter Analysis Engineering.” NASA/TM-20250000899. ntrs.nasa.gov/citations/20250000899
Belvin, W.K. (1995). “Spacecraft Jitter Attenuation Using Embedded Piezoelectric Actuators.” NASA-TM-111574, Langley RC. ntrs.nasa.gov/citations/19960024186
ESA Standards & European Research
ECSS-E-HB-32-26A (2013). “Spacecraft Mechanical Loads Analysis Handbook.” ESA Requirements and Standards Division. Covers microvibration sources, definitions, and analysis approaches.
Calvi, A. et al. (2013). “Microvibration Environment and Testing: Lessons Learned.” European Conference on Spacecraft Structures, Materials & Environmental Testing.

## Slide 44
Vibrationdata
References and Further Reading (cont)
Key documents, handbooks, and peer-reviewed references for spacecraft jitter engineering
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
44
Isolators & Hardware
Davis, L.P. et al. (1994). “D-Strut™: A Three-Parameter Passive Viscous Damper for Spacecraft.” SPIE Smart Structures & Materials, Vol. 2445, pp. 161–175. (Honeywell/HST RWA isolation heritage.)
Davis, L.P. (1986). U.S. Patent 4,760,996, “Damper and Isolator.” Honeywell. (Original D-Strut two-parameter viscous isolator.)
Ross, R.G., Jr. (2003). “Cryocooler Vibration and Microphonics: A Tutorial.” JPL. trs.jpl.nasa.gov (JPL Technical Reports Server).
Textbooks & Irvine References
Irvine, T. (2014). “Spacecraft On-orbit Vibration.” Vibrationdata Blog. blog.vibrationdata.com/2014/06/12/spacecraft-on-orbit-vibration/
Irvine, T. VibrationData MATLAB GUI Package and Technical eBooks. blog.vibrationdata.com/2025/11/27/toms-ebooks/ (SRS, FDS, fatigue, structural dynamics.)
Craig, R.R. & Bampton, M.C.C. (1968). “Coupling of Substructures for Dynamic Analysis.” AIAA Journal, 6(7), 1313–1319. (Foundational Craig-Bampton substructuring reference.)
Meirovitch, L. (1997). Principles and Techniques of Vibrations. Prentice Hall. (Standard structural dynamics textbook.)

## Slide 45
PART 5
Worked Examples
Putting numbers on the governing relations — from imbalance force to MTF loss
45

## Slide 46
Vibrationdata
Worked Example: Reaction Wheel Imbalance
Putting numbers on the F = Cᵢ·Ω² relation — imbalance force scales with the square of wheel speed
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
46
Given
Static imbalance Uₛ = 1.8 g·cm = 1.8×10⁻⁵ kg·m
Dynamic imbalance Ud = 80 g·cm² = 8.0×10⁻⁶ kg·m²
Wheel speed = 4000 rpm
Ω = 4000·2π/60
= 418.9 rad/s
f₁ = Ω/2π = 66.7 Hz
F = Uₛ·Ω² = 3.16 N
M = U_d·Ω² = 1.40 N·m
Takeaway: Imbalance force grows with Ω² — doubling wheel speed quadruples the disturbance force.

## Slide 47
Vibrationdata
Worked Example: Force → Jitter Through an FRF
Carrying the 3.16 N imbalance line through a structural FRF and combining contributors by RSS
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
47
Step-by-Step
Take F = 3.16 N at f₁ = 66.7 Hz from the imbalance example
Mount-to-bench FRF off-resonance: |H| = 1.5 nrad/N
Off-resonance tilt: θ₁ = 3.16 N × 1.5 nrad/N = 4.7 nrad
Near a 70 Hz mode (Q ≈ 6) the FRF rises 6×:
Resonant-crossing tilt: θ₁ = 28 nrad
Broadband random contribution (Miles example): 9 nrad RMS
RSS Combination
Total = √( ² + ²)
= √(28² + 9²)
= 29.4 nrad RMS
Compared to Allocation
JWST-class LOS budget: ~7–14 nrad RMS
Predicted 29.4 nrad RMS at the resonance crossing exceeds the allocation by ~2–4×
Result: define a no-spin-zone exclusion band around the 70 Hz crossing
is the harmonic tilt/jitter contribution from the discrete imbalance line
is the random broadband tilt/jitter contribution

## Slide 48
Vibrationdata
Worked Example: Random Response (Miles)
Broadband RMS from a flat input PSD through an isolated Single-degree-of-freedom (SDOF) System
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
48
Given
Flat input A = 1×10⁻⁸ g²/Hz
Isolator fₙ = 15 Hz, ζ = 0.05 (Q = 10)
Grms =
= √[(π/2)(15)(10) (1×10⁻⁸)]
= 1.54 milli-g rms
Corresponding RMS displacement
≈ 1.70×10⁻³ mm ≈ 1.70 µm
Links directly to the sway-space trade of the isolation slides

## Slide 49
Vibrationdata
Worked Example: Isolator Transmissibility
Hard numbers on the damping trade — evaluating T at the 66.7 Hz wheel line for an fₙ = 15 Hz isolator
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
49
High-Frequency Attenuation
ζ = 0.05: T = 0.054 → −25 dB
ζ = 0.20: T = 0.094 → −20.5 dB
Resonant Peak (r = 1)
ζ = 0.05: T ≈ 1/(2ζ) = 10
ζ = 0.20: T ≈ 2.5
Takeaway: Heavier damping cuts the peak ~4× but costs ~5 dB of high-frequency attenuation.

## Slide 50
Vibrationdata
Worked Example: Modular Transfer Function Reduction From Jitter
The Gaussian-jitter MTF factor MTFⱼ = exp[−2π²σ²f²], evaluated at the Nyquist frequency
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
50
At Nyquist (f = 0.5 cyc/px)
MTFⱼ = exp[−2π²σ²f²]
σ = 0.1 px → MTFⱼ = 0.951 (5% loss)
σ = 0.2 px → MTFⱼ = 0.821 (18% loss)
σ = 0.3 px → MTFⱼ = 0.641 (36% loss)
σ is the standard deviation of the line-of-sight jitter displacement, typically expressed in pixels (or in the same spatial units as the spatial frequency f).
Takeaway: Sub-pixel jitter is not negligible — 0.2 px already removes ~18% of contrast at Nyquist, which is why fine-pointing budgets are stated in milli-pixels or nanoradians.

## Slide 51
Vibrationdata
Worked Example: Acceleration Ratio
Conservation of angular momentum — the acceleration ratio equals the inverse ratio of moments of inertia
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
51
Setup
Wheel moment of inertia = 0.02 kg·m²
Spacecraft inertia about that axis = 500 kg·m²
Commanded wheel angular acceleration = 100 rad/s²
The Resulting spacecraft angular acceleration
= (0.02 / 500)(100)
= 4×10⁻³ rad/s²
Inertia ratio
25,000 : 1
The spacecraft’s angular acceleration is 25,000× smaller than the wheel’s — the same inverse-inertia leverage that makes a small flywheel an effective fine-pointing actuator.
Takeaway: Large is exactly why reaction wheels give precise, low-disturbance control authority.

## Slide 52
PART 6
Case Histories
Four flight programs where microvibration drove the design — and one where it ended the mission
52

## Slide 53
Hubble Space Telescope

## Slide 54
Case History: Hubble Solar-Array Thermal Snap
Vibrationdata
The archetype — a thermal disturbance, not a wheel, broke the pointing budget
Hubble Space Telescope
ROLE
0.007 arcsec pointing-class optical observatory (LEO, 97-min orbit)
ONSET
Jitter seen immediately after April 1990 deployment
FIX FLOWN
PCS software (1990) + new ESA arrays, SM1 Dec 1993
Disturbance
Bi-stem solar-array booms heating unevenly at each day/night terminator crossing — ~30 thermal cycles per day, −150 °C to +200 °C swings.
Mechanism
Stored thermal/mechanical energy released as an abrupt “snap” that excited the array's primary modes; the body reacted against the flexible arrays — internal vibration was negligible.
Consequence
Disturbance far exceeded the jitter spec; FGSs lost interferometric lock, forcing coarse-track mode that prematurely wore the star-selector bearings. Science lost ~1/3 of each orbit.
Takeaway: The dominant disturbance source is not always a reaction wheel — a flexible appendage plus a thermal transient can dominate the entire line-of-sight budget.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
54

## Slide 55
Chandra X-ray Observatory

## Slide 56
Case History: Chandra Reaction-Wheel Isolation
Vibrationdata
Designing the disturbance out — passive hexapod isolators at the source
Chandra X-ray Observatory (AXAF)
ROLE
Third Great Observatory; grazing-incidence X-ray optics, launched 1999
SOURCE
Six reaction wheels feeding a jitter-sensitive optical bench
STRATEGY
Passive vibration isolation at each wheel interface
Disturbance
Reaction-wheel imbalance and bearing tones transmitted from the wheel assemblies into the spacecraft central structure across a broad speed range.
Solution
A hexapod (6-strut) passive isolator beneath each of the six wheels — unit-level transmissibility requirements were derived top-down from the image-quality flowdown.
Outcome
Wheel jitter at the optics was suppressed enough to meet imaging performance without an active control loop. The same hexapod approach was later carried into JWST's wheel isolator.
Takeaway: When the source is a known wheel set, a passive isolator sized from a requirement flowdown is often sufficient — and far simpler than active control.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
56

## Slide 57
James Webb Space Telescope

## Slide 58
Case History: JWST Two-Stage Isolation
Vibrationdata
Layered isolation — wheels and a cryocooler, verified against a hard mas budget
James Webb Space Telescope
ROLE
6.6 m IR observatory at Sun–Earth L2; launched Dec 2021
SOURCES
Reaction wheels + MIRI cryocooler compressor (≈7 K, JT/pulse-tube)
REQUIREMENT
7 mas RMS radial line-of-sight jitter
Disturbance
Broadband wheel imbalance plus narrowband cryocooler compressor tones — both above the attitude-control bandwidth, so they must be handled mechanically.
Solution
Two passive isolation layers: a wheel isolator (≈7 Hz rocking / 12 Hz translation corners) supporting all six wheels, and a 1 Hz isolator at the deployment-tower / bus interface.
Outcome
Commissioning measured ~1.04 mas RMS radial jitter — near the measurement noise floor, well inside the 7 mas spec, with no cryocooler retuning needed.
Takeaway: Stacking isolation stages (wheel-level + spacecraft-level) and reserving wheel-speed/compressor exclusion zones delivered ~7× margin against the flight budget.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
58

## Slide 59
Kepler Space Telescope

## Slide 60
Case History: Kepler Reaction-Wheel Loss
Vibrationdata
The other failure mode — when the pointing actuator itself degrades
Kepler Space Telescope
ROLE
0.95 m photometer; ~20 ppm precision on mag-12 stars (6.5 h)
EVENTS
Wheel #2 failed Jul 2012; wheel #4 failed May 2013
RESULT
Primary mission ended; reborn as the two-wheel K2 mission
Disturbance
Reaction-wheel bearing friction rose past acceptable levels. Constant friction can be trimmed by the ACS; variable friction cannot — it renders a wheel unusable.
Mechanism
Three good wheels are the minimum for fine three-axis pointing. With only two, solar radiation pressure could no longer be balanced about the boresight without thruster firing.
Consequence
Pointing precision degraded by roughly a factor of 3–4, ending precise transit photometry. K2 recovered partial capability by balancing the craft against solar pressure.
Takeaway: The disturbance source and the pointing actuator can be the same hardware. Bearing health and wheel redundancy are pointing-budget items, not just reliability items.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
60

## Slide 61
Vibrationdata
Case-History Synthesis: Four Lessons
What each flight program teaches about where microvibration really comes from
Hubble — Thermal Snap
Dominant source was a flexible appendage + thermal transient, not a wheel
Lesson: budget appendage dynamics and terminator-crossing transients, not just rotating machinery
Chandra — Passive Isolation
Hexapod isolators sized from an image-quality flowdown met spec with no active loop
Lesson: a passive isolator from a requirement flowdown is often sufficient and far simpler
JWST — Stacked Isolation
Wheel-level + spacecraft-level stages plus exclusion zones gave ~7× margin
Lesson: layering isolation stages and reserving speed/compressor zones compounds the margin
Kepler — Actuator Loss
Variable wheel-bearing friction ended precise pointing — source and actuator were the same part
Lesson: bearing health and wheel redundancy are pointing-budget items, not just reliability items
Takeaway: The disturbance source is not always a reaction wheel, the actuator can be the source, and stacked passive isolation goes a long way — design for the whole chain.
Spacecraft On-Orbit Vibration | blog.vibrationdata.com
61